## Slide 1: WF on sync raster for NR
Agenda Item: 7.3.2.3
Document for: Approval
Source: Ericsson
3GPP TSG-RAN WG4 #86bis Tdoc R4-1805980
Melbourne, Australia, 16 – 20 April 2018

## Slide 2: Input on Sync raster offset
ZTE [1] 100 kHz Sees no big difference
Samsung [2] 100 kHz Aligns with 100 kHz raster
Huawei [3] 70 kHz Feasible for multiple solutions
Ericsson [4] 70 kHz Sees no big difference
Vivo [5] 85/95 kHz
Intel [6] 100 kHz Sees no big difference
Mediatek [7] 70 kHz Slightly less complex (single scan)
LG [8] 100 kHz Better for HS and low cost devices
Nokia [9] 100 kHz Aligns with 100 kHz raster and LTE
Qualcomm [10] 100 kHz Aligns with 100 kHz raster and LTE

## Slide 3: Sync raster separation
Proposal in [10] to consider larger separation than 900 kHz to reduce the total number of points, specifically 1200 MHz
All possibilities up to 1400 kHz have been investigated, with a 100 kHz shift applied: 900, 1000, 1100, 1200, 1300, 1400 kHz
The following criteria were used to eliminate invalid choices:
  At least one valid SSB within the carrier for each channel raster entry in all re-farming bands, for all BS Channel BW/SCS combinations
  SSB position should give SCS alignment between SS and data
The following two choices remain
  900 kHz with +/-100 kHz shift
  1200 kHz with +/-100 kHz shift and the raster offset by 150 kHz

## Slide 4: Summary and way forward (Sync raster separation & shift)
In order to reduce the number of sync raster entries as much as possible, the highest sync raster separation was chosen
  Way forward:
  1200 kHz with +/-100 kHz shift and the raster offset by 150 kHz

## Slide 5: Overlap in 2400-2700 MHz
Problem identified in [2] and [5]
Overlapping range of the two SS rasters within the freqeuncy range 2400-2700 MHz: 900 and 1440 kHz raster separation
Raster positions may be as close as 40 kHz, causing ambiguity
Multiple searches would be needed in overlapping bands
NOTE: Agreement in Way-Forward (R4-1801316):
For step size <N>, GSCN that are multiples of N are selected (this ensures overlapping bands have same GSCN)
PROPOSAL from [2]: Revise raster separation in 2400-3000 MHz to align with the re-farming bands

## Slide 6: Summary and way forward (Overlap in 2400-2700 MHz)
The existing overlap in the range 2400-3000 MHz is inefficient and not future proof
With the new choice of raster separation, the difference is small compared to existing raster
The sync raster offset (150 kHz) is chosen as a multiple of both 15 and 30 kHz SCS
The shifted raster points do not apply in with SCS based channel raster
  Way forward:
  The 1200 kHz sync raster (offset by 150 kHz) is applied for all bands in the range 2400-3000 MHz

## Slide 7: Way forward summary
Sync raster for re-farming bands:
  1200 kHz raster with +/-100 kHz shift and the raster offset by 150 kHz
Sync raster in 2400 – 3000 MHz
  Same raster defined as in 0 – 2400 MHz
  For bands with SCS-based channel raster, the shifted points do not apply: 1200 kHz raster offset by 150 kHz

## Slide 8: References
R4-1803654, "Considerations on SS raster shift in re-farming bands" (ZTE Corporation, Sanechips).
R4-1803838, "Discussion on open issues of sync rasters" (Samsung).
R4-1803890, "On synchronization raster shift" (Huawei, HiSilicon).
R4-1804042, "Sync raster shift in re-farming bands" (Ericsson).
R4-1804076, "Discussion on NR sync raster shift for frequency range 0-2700MHz" (vivo).
R4-1804111, "On NR synchronization raster for FR1 re-farming bands" (Intel Corporation).
R4-1804329, "NR sync raster shift" (MediaTek Inc.).
R4-1804497, "Discussion on sync raster shift for LTE re-farming bands" (LG Electronics Inc.).
R4-1804946, "On Sync raster offset" (Nokia, Nokia Shanghai Bell).
R4-1805384, "Sync Raster for NR" (Qualcomm Incorporated).