## Slide 1: WF on RRM with network-based CRS interference mitigation
Ericsson, Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #86bis R4-1806016
Melbourne, Australia, 16th - 20th April, 2018
Agenda Item: 6.27.2

## Slide 2: Background
AllowedMeasBandwidth can be used to prevent UEs measuring over a large BW in intra-frequency and inter-frequency neighbor cells
  Earlier agreed (R4-1709102):
    If the UE is configured with widebandRSRQ-Meas to measure WB-RSRQ then the UE shall assume that CRS are available in the measured cell over the AllowedMeasBandwidth (e.g., 50 RBs or larger),
    Otherwise CRS may be transmitted over 6 RBs in neighbor cells (AllowedMeasBandwidth is 6 RBs)

## Slide 3: Agreement
The CRS muting can only be enabled in cells on some dedicated carriers. Legacy UEs (Rel-14 or earlier UEs) or UE not capable of supporting network-based CRS interference mitigation shall not be served by and shall not be accessing cell(s) on the dedicated carrier where network-based CRS interference mitigation is used
Send LS to RAN2 (cc to RAN1)

## Slide 4: Signalling Support
The signalling support for network-based CRS interference mitigation includes:
  Information from the network to make the UE aware of whether network-based CRS interference mitigation is enabled or not:
    The following SI information is needed at least for UE in RRC_IDLE:
      Network-based CRS interference mitigation is enabled or disabled in the serving cell
      NOTE: This information should be provided to the UE as early as possible
    In RRC_CONNECTED, the dedicated RRC signaling (e.g., neighCellsCRS-Info and neighCellsCRS-InfoSCell in TS 36.331) is enhanced to include an indication whether the network-based CRS interference mitigation is enabled or not in the serving cell(s), including PSCell and SCells, and one or more neighbor cells
    In RRC_CONNECTED, the UE should be configured with CRS muting information for the target cell e.g. in handover command

## Slide 5: RAN4 Requirements
RAN4 will specify applicable requirements for Rel-15 UEs capable of supporting network-based CRS interference mitigation and define the corresponding warm-up/cool-down subframes in TS 36.133 for RRC_IDLE and RRC_CONNECTED on dedicated carriers where CRS muting is used