## Slide 1: WF on NR CSI feedback tests
Intel
3GPP TSG-RAN WG4#88 Meeting
Gothenburg, Sweden, 20 – 24 August 2018 Agenda Item: 7.13.1.5
R4-1809801

## Slide 2: Background
Agreements related to the NR UE CSI performance requirements were reached in the WF [1] as below:
First focused on the mandatory features
Overall Test Configuration & Scope
  First priority focused on:
    NZP CSI-RS for channel measurement CSI-IM for interference measurement
    CSI report types: periodic CSI report and aperiodic CSI report
    CSI-RS resources types: periodic and aperiodic
PMI reporting
  In Rel-15 focused on Type-I single panel codebook
In RAN4-AH-1807 Meeting (July 2018), a WF [2] on NR UE CSI requirements was approved regarding the initial simulation assumptions for FR1 and FR2 CQI/PMI/RI tests. Companies were encouraged to provide initial simulation results and views on the assumptions and scenarios for NR UE CSI feedback tests.
This WF provides NR FR1/FR2 CQI/PMI/RI reporting test tables for simulation assumptions alignment.
[1] R4-1808027, “Way forward on NR UE demodulation and CSI requirements”, Ericsson, May 2018
[2] R4-1809358, “Way forward on NR UE CSI requirements”, Samsung, July 2018

## Slide 3: Simulation Assumptions for CQI
Table 1 Test parameters for static CQI reporting performance requirements
Note: For CQI reporting tests, DMRS configuration needs to be specified.
Parameters | FR1 FDD | FR1 TDD | FR2 TDD
CBW[MHz]/SCS[KHz] | 10MHz/15KHz | 40MHz/30KHz | 100MHz/120KHz
DL UL configuration | N/A | DDDSU “S” slot is not scheduled for PDSCH | DDDSU “S” slot is not scheduled for PDSCH
Modulation | 256QAM table | 256QAM table | 64QAM table
CSI-RS/CSI-IM periodicity and slot offset | [5/0] | [5/0] | [5/0]
Propagation channel | AWGN TS_36.101_Static | AWGN TS_36.101_Static | AWGN TS_36.101_Static
Correlation and antenna configuration | 2×2 | 2×2 | 2×2
Number of Tx CSI-RS ports | 2 | 2 | 2
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density | [FD-CDM2/density 1] | [FD-CDM2/density 1] | [FD-CDM2/density 1]
reportConfigType | periodic | periodic | periodic
Reporting periodicity and slot offset | [5/1] | [5/1] | [5/1]
Rank | 2 | 2 | 2
Codebook Restriction | 010000 (fixed rank2) | 010000 (fixed rank2) | 010000 (fixed rank2)
PTRS presence | OFF | OFF | ON
CSI-RS Type | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement
CSI type | Type I single-panel | Type I single-panel | Type I single-panel
PMI frequency granularity | Wideband | Wideband | Wideband
CQI frequency granularity | Wideband | Wideband | Wideband

## Slide 4: Simulation Assumptions for PMI
Table 2 Test parameters for PMI reporting performance requirements
Parameters | FR1 FDD | FR1 TDD | FR2 TDD
CBW[MHz]/SCS[KHz] | 10MHz/15KHz | 40MHz/30KHz | 100MHz/120KHz
DL UL configuration | N/A | DDDSU “S” slot is not scheduled for PDSCH | DDDSU “S” slot is not scheduled for PDSCH
Modulation | 256QAM table | 256QAM table | 64QAM table
MCS | MCS13 | MCS13 | MCS4
CSI-RS/CSI-IM periodicity and slot offset | [5/0] | [5/0] | [5/0]
Propagation channel | TDL 30ns, 5Hz | TDL 30ns, 5Hz | TDL 30ns, 5Hz
Correlation and antenna configuration | 8×2 XPL high | 8×2 XPL high | 2×2 FFS
Number of Tx CSI-RS ports | 8 | 8 | 2
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density | [FD-CDM4/density 1] | [FD-CDM4/density 1] | [FD-CDM2/density 1]
reportConfigType | aperiodic | aperiodic | aperiodic
Reporting periodicity and slot offset | [5/1] | [5/1] | [5/1]
Rank | 2 | 2 | 1
Codebook Mode | 1 | 1 | N/A
Codebook Restriction | N/A | N/A | N/A
(N1, N2) | (2, 2) | (2, 2) | N/A
(O1, O2) | (4, 4) | (4, 4) | N/A
Reporting granularity | Wideband | Wideband | Wideband
PTRS presence | OFF | OFF | ON
CSI-RS Type | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement
CSI type | Type I single-panel | Type I single-panel | Type I single-panel
PMI frequency granularity | Wideband | Wideband | Wideband
CQI frequency granularity | Wideband | Wideband | Wideband

## Slide 5: Simulation Assumptions for RI
Table 3 Test parameters for RI reporting performance requirements
Parameters | FR1 FDD | FR1 TDD | FR2 TDD
CBW[MHz]/SCS[KHz] | 10MHz/15KHz | 40MHz/30KHz | 100MHz/120KHz
DL UL configuration | N/A | DDDSU “S” slot is not scheduled for PDSCH | DDDSU “S” slot is not scheduled for PDSCH
Modulation | 256QAM table | 256QAM table | 64QAM table
CSI-RS/CSI-IM periodicity and slot offset | [5/0] | [5/0] | [5/0]
Propagation channel | TDL 30ns, 5Hz | TDL 30ns, 5Hz | TDL 30ns, 5Hz
Correlation and antenna configuration | 2×2 ULA Low | 2×2 ULA Low | 2×2 FFS
Number of Tx CSI-RS ports | 2 | 2 | 2
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density | [FD-CDM4/density 1] | [FD-CDM4/density 1] | [FD-CDM2/density 1]
reportConfigType | periodic | periodic | periodic
Reporting periodicity and slot offset | [5/1] | [5/1] | [5/1]
Rank | 1, 2 | 1, 2 | 1, 2
Codebook Restriction | 010011 | 010011 | 010011
FRC | Follow CQI/PMI | Follow CQI/PMI | Follow CQI/PMI
Reporting granularity | Wideband | Wideband | Wideband
PTRS presence | OFF | OFF | ON
CSI-RS Type | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement | - NZP CSI-RS for channel measurement - CSI-IM for interference measurement
CSI type | Type I single-panel | Type I single-panel | Type I single-panel
PMI frequency granularity | Wideband | Wideband | Wideband
CQI frequency granularity | Wideband | Wideband | Wideband