## Slide 1: Way forward on NR PDCCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20 – 24 August, 2018
R4-1811395

## Slide 2: Agreements
Aggregation levels
  AL2, AL4, AL8
  FFS for AL16
Applicability of 4Rx PDCCH demodulation requirements
  Using similar test condition as LTE, 4Rx NR PDCCH demodulation performance tests only if there are continuous PDSCH grants in every slot.
REG Bundle size for 4Rx PDCCH test cases
  Agreement in AH1807: REG bundle size =6 for non-interleaved, 2 for interleaved
  FFS REG bundle size for all the 4Rx PDCCH test cases is changed to 6.

## Slide 3: Agreements
Test configurations for 1 symbol PDCCH test case(s)
  Introduce additional requirements with 1 symbol control channel for FR1 FDD with 10MHz and 15kHz SCS (for LTE-NR coexistence scenario)
  See Test 12 in page 4 for the detailed parameters

## Slide 4: Update of simulation assumption
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
1 | 15 | 1_0 | 24 | 39 | 2 | 2 | Non-interleaved | 6 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
2 | 15 | 1_0 | 24 | 39 | 2 | 4 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
3 | 15 | 1_1 | 24 | [50] | 2 | 2 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
4 | 15 | 1_1 | 48 | [50] | 2 | 4 | Non-interleaved | 6 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
5 | 15 | 1_1 | 48 | [50] | 2 | 8 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
6 | 30 | 1_0 | 102 | 41 | 1 | 2 | Interleaved | 2 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
7 | 30 | 1_1 | 102 | [52] | 1 | 4 | Interleaved | 2 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
8 | 30 | 1_1 | 102 | [52] | 1 | 8 | Interleaved | 2 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
9 | 120 | 1_0 | [60] | 41 | 1 | 2 | Interleaved | 2 | TBD | 1x2 Low | NA
10 | 120 | 1_1 | [60] | [51] | 1 | 4 | Interleaved | 2 | TBD | 1x2 Low | NA
11 | 120 | 1_1 | [60] | [51] | 1 | 8 | Interleaved | 2 | TBD | 2x2 Low | NA
12 | 15 | 1_0 | 48 | 39 | 1 | 4 | Non-interleaved | 6 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low