## Slide 1: WF for DC_3A_n3A in Rel.16 CHTTL, Skyworks
3GPP TSG-RAN WG4 Meeting #88 R4-1811500 Gothenburg, SE, 20th – 24th August, 2018

## Slide 2: Backgrounds
DC_3A_n3A is introduced in Rel.15 with single UL switched support
It is agreed to continue studying dual uplink transmission mode for DC_3A_n3A in Rel.16
In the previous RAN4 meetings, several agreements related to the intra-band EN-DC were agreed for specific bands only

## Slide 3: Proposals (1/4)
Introduce new BCS set 1 for DC_3A_n3A in Rel.16
Dual uplink transmission mode is supported in Rel.16
  Single switch UL mode is also allowed based on the same principle as in Rel.15 inter-band EN-DC
 |  | E-UTRA – NR configuration / Bandwidth combination set |  |  |  | 
Downlink EN-DC configuration | Uplink EN-DC configurations | Component carriers in order of increasing carrier frequency |  |  | Maximum aggregated bandwidth (MHz) | BCS
 |  | Channel bandwidths for LTE carrier (MHz) | Channel bandwidths NR for carrier (MHz) | Channel bandwidths for LTE carrier (MHz) |  | 
DC_3A_n3A | DC_3A_n3A |  | 5, 10, 15, 20, 25, 30 | 5, 10, 15, 20 | 50 | 0
 |  |  | 5, 10, 15, 20, 25, 30 | 5, 10, 15, 20 | 50 | 1
 |  | 5, 10, 15, 20 | 5, 10, 15, 20, 25, 30 |  |  | 

## Slide 4: Proposals (2/4)
RF reference architectures
  Both 2PA/antennas and 1PA/antenna architectures are considered when defining MPR and MSD for DC_3A_n3A
  2PA architecture is prioritized
    4 dB post-PA insertion loss on each Tx chain
    10 dB antenna isolation
  Duplexer Isolation
    At least 50dB isolation
      Whether the feasibility of 55dB isolation can be further discussed and considered with the possible advances in duplexer technology

## Slide 5: Proposals (3/4)
MPR requirement for DC_3A_n3A
  MPR for DC_3A_n3A is developed with consideration of varying gap lengths and RB allocations
  The following limitations are considered when addressing MPR requirement for DC_3A_n3A
    ACLR overlap
    -13dBm/MHz SEM
    -25dBm/MHz SEM
    -30dBm/MHz spurious emissions
    -50dBm/MHz own band protection (only for 1PA case)
  Self-desentization is specified with MSD and no MPR is used to mitigate MSD
  At least MPR will be defined for Type 1 and Type 2 UEs

## Slide 6: Proposals (4/4)
MSD for DC_3A_n3A
  DFT-s-OFDM 15KHz SCS waveforms are used for NR
  12RB UL configuration is used as in [4]
  One worst case test point for IMD3 and IMD5 [4]
    First 5MHz UL sub-block at center 1737.5MHz (RB start = 12), Second 5MHz UL sub-block at center1782.5MHz (RB start = 0)
  Another test point for receiver sensitivity and PA noise [4]
    First 5MHz UL sub-block at 1772.5MHz (RB end = 24), Second 5MHz UL sub-block at 1782.5MHz (RB start = 0)
  Other test points are not precluded

## Slide 7: Referense
  [1] R4-1810372, “Initial analysis for A-MPR and MSD for dual uplink transmission of DC_3_n3”, CHTTL, RAN4#88
  [2] R4-1805761, “WF for UE RF AH specific for DC_(n)71B”, Nokia, RAN4#86bis
  [3] R4-1805774, “WF on B41/n41 intra-band EN-DC requirements”, SPRINT Corporation, RAN4#86bis
  [4] R4-1809796, “MSD and AMPR Issues for DC_3A_n3A”, Skyworks Solutions Inc. , RAN4#88