## Slide 1: Receiver directional TT and out of band blocking MU and TT
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting#88
Gothenburg, Sweden, 20 – 24 August 2018
Agenda Item: 6.1.1
R4-1811676

## Slide 2: Agreed way forward on MU for eAAS and NR FR1 OTA receiver directional requirements in RAN4 AH-1807
MU for dynamic range: Adopt conducted MU for OTA.
Conducted MU: Conducted MUs for wanted and interfering signals already include 95% confidence level, hence no need to multiply MU by 1.96 for summation.
Mismatch uncertainty: Use the EIS measurement uncertainty from the source ‘Impedance mismatch in the transmitting chain’ and ‘Standing wave between DUT and test range antenna’ recorded in TR 37.842 as the mismatch uncertainty for IAC and CATR, respectively, for the frequency range below 4.2 GHz for both conducted and OTA parts.
Need for PA: Do not include additional PA MU.
Companies are encouraged to input EIS MU for NR FR1 (4.2GHz < f ≦ 6GHz) in RAN4 meeting#88. If no further analysis on NR FR1 according to the agreed timeline, the same MU budget as eAAS (3GHz < f ≦ 4.2GHz) can be reused for NR FR1 (3GHz < f ≦ 6GHz).

## Slide 3: Agreed MU for eAAS and NR FR1 OTA receiver directional requirements in RAN4 AH-1807
 | Expanded uncertainty ue [dB] |  | 
 | f ≦ 3GHz | 3GHz < f ≦ 4.2GHz | 4.2GHz < f ≦ 6GHz
receiver dynamic range | 0.3 | 0.3 | TBD
adjacent channel selectivity, narrowband blocking, and in-channel selectivity | 1.7 | 2.1 | TBD
in-band blocking | 1.9 | 2.2 | TBD
receiver intermodulation | 2.0 | 2.6 | TBD

## Slide 4: Agreed way forward on TT for eAAS and NR FR1 OTA receiver directional requirements in RAN4 AH-1807
TT for each requirement is within the range:
  Conducted TT ≦ OTA TT ≦ Conducted TT + (OTA MU - Conducted MU)
Target is TT shall be decided in RAN4 meeting#88

## Slide 5: Agreed way forward on TT for eAAS and NR FR1 OTA receiver directional requirements in RAN4 AH-1807
 | Test Tolerance [dB] |  |  |  |  |  |  |  | 
 | f ≦ 3GHz |  |  | 3GHz < f ≦ 4.2GHz |  |  | 4.2GHz < f ≦ 6GHz |  | 
 | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU
receiver dynamic range | 0.3 | 0.3 | 0 | 0.3 | 0.3 | 0 | 0.3 | TBD | TBD
in-channel selectivity | 1.4 | [1.4 -> 1.7] | 0.3 | 1.8 | [1.8 -> 2.1] | 0.3 | 2.5 | TBD | TBD
adjacent channel selectivity and narrowband blocking | 0 | [0 -> 0.3] | 0.3 | 0 | [0 -> 0.3] | 0.3 | 0 | TBD | TBD
in-band blocking | 0 | [0 -> 0.3] | 0.3 | 0 | [0 -> 0.2] | 0.2 | 0 | TBD | TBD
receiver intermodulation | 0 | [0 -> 0.2] | 0.2 | 0 | [0 -> 0.2] | 0.2 | 0 | TBD | TBD

## Slide 6: Further analysis for MU for eAAS and NR FR1 OTA receiver requirements provided in RAN4#88
[1] R4-1809693, “Proposals on MU for eAAS OTA receiver out-of-band blocking requirement”, Nokia, Nokia Shanghai Bell.
[2] R4-1810362, “MU of OTA OBUE, SEM, ACLR absolute requirement”, NTT DOCOMO, INC.
[3] R4-1810583, “TBDs on acceptable uncertainty of Test System (4.1.2)”, Huawei, HiSilicon.
[4] R4-1810952, “Test Equipment uncertainty values for FR1 EIS MU”, Keysight Technologies.
[5] R4-1811076, “out of band blocking MU analysis”, Huawei.

## Slide 7: Way forward on MU for NR FR1 (4.2GHz < f ≦ 6GHz)
With
1.96 0.58 [3]
And
1.96 0.28 for IAC [2]

## Slide 8: MU eAAS and NR FR1 (4.2GHz < f ≦ 6GHz) OTA receiver requirements for IAC
 | Expanded uncertainty ue [dB] |  | 
 | f ≦ 3GHz | 3GHz < f ≦ 4.2GHz | 4.2GHz < f ≦ 6GHz
receiver sensitivity and reference sensitivity | 1.2 | 1.3 | 1.5
receiver dynamic range | 0.3 | 0.3 | 0.3
adjacent channel selectivity, narrowband blocking, and in-channel selectivity | 1.7 | 2.0 | 2.3
in-band blocking | 1.8 | 2.1 | 2.4
receiver intermodulation | 2.0 | 2.5 | 3.1

## Slide 9: MU eAAS and NR FR1 (4.2GHz < f ≦ 6GHz) OTA receiver requirements for CATR
 | Expanded uncertainty ue [dB] |  | 
 | f ≦ 3GHz | 3GHz < f ≦ 4.2GHz | 4.2GHz < f ≦ 6GHz
receiver sensitivity and reference sensitivity | 1.3 | 1.4 | 1.6
receiver dynamic range | 0.3 | 0.3 | 0.3
adjacent channel selectivity, narrowband blocking, and in-channel selectivity | 1.7 | 2.1 | 2.4
in-band blocking | 1.9 | 2.2 | 2.5
receiver intermodulation | 2.0 | 2.6 | 3.2

## Slide 10: Final MU for eAAS and NR FR1 (4.2GHz < f ≦ 6GHz) OTA receiver requirements
 | Expanded uncertainty ue [dB] |  | 
 | f ≦ 3GHz | 3GHz < f ≦ 4.2GHz | 4.2GHz < f ≦ 6GHz
receiver sensitivity and reference sensitivity | 1.3 | 1.4 | 1.6
receiver dynamic range | 0.3 | 0.3 | 0.3
adjacent channel selectivity, narrowband blocking, and in-channel selectivity | 1.7 | 2.1 | 2.4
in-band blocking | 1.9 | 2.2 | 2.5
receiver intermodulation | 2.0 | 2.6 | 3.2

## Slide 11: Way forward on MU for eAAS and NR FR1 OTA out-of-band blocking requirement
Where is the additional uncertainty for the out-of-band interferer including factors like PA, interferer transmit antenna and frequency variation
And can be obtained for IAC as shown in spreadsheet on next slide

## Slide 12: for IAC

## Slide 13: Final MU for eAAS and NR FR1 OTA out-of-band blocking requirement
 | Expanded uncertainty ue [dB] |  | 
Wanted signal frequency range: | fwanted ≤ 3GHz | 3GHz < fwanted ≤ 4.2GHz | 4.2GHz < fwanted ≤ 6.0GHz
Interfering signal frequency range: |  |  | 
1MHz < finterferer ≤ 3GHz | 2.0 | 2.0 | 2.2
3GHz < finterferer ≤ 6GHz | 2.1 | 2.1 | 2.3
6GHz < finterferer ≤ 12.75GHz | 3.5 | 3.6 | 3.6

## Slide 14: Comparison on conducted Vs OTA MU for eAAS and NR FR1 OTA receiver directional requirements
 | Expanded uncertainty ue [dB] |  |  |  |  |  |  |  | 
 | f ≦ 3GHz |  |  | 3GHz < f ≦ 4.2GHz |  |  | 4.2GHz < f ≦ 6GHz |  | 
 | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU
receiver sensitivity and reference sensitivity | 0.7 | 1.3 | 0.6 | 1 | 1.4 | 0.4 | 1.5 | 1.6 | 0.1
receiver dynamic range | 0.3 | 0.3 | 0 | 0.3 | 0.3 | 0 | 0.3 | 0.3 | 0
in-channel selectivity | 1.4 | 1.7 | 0.3 | 1.8 | 2.1 | 0.3 | 2.5 | 2.4 | 0.1
adjacent channel selectivity and narrowband blocking | 1.4 | 1.7 | 0.3 | 1.8 | 2.1 | 0.3 | 2.5 | 2.4 | 0.1
in-band blocking | 1.6 | 1.9 | 0.3 | 2.0 | 2.2 | 0.2 | 2.7 | 2.5 | 0.2
receiver intermodulation | 1.8 | 2.0 | 0.2 | 2.4 | 2.6 | 0.2 | 3.3 | 3.2 | 0.1

## Slide 15: Way forward on TT for eAAS and NR FR1 OTA receiver directional requirements
 | Test Tolerance [dB] |  |  |  |  |  |  |  | 
 | f ≦ 3GHz |  |  | 3GHz < f ≦ 4.2GHz |  |  | 4.2GHz < f ≦ 6GHz |  | 
 | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU
receiver sensitivity and reference sensitivity | 0.7 | 1.3 | 0.6 | 1 | 1.4 | 0.4 | 1.5 | 1.6 | 0.1
receiver dynamic range | 0.3 | 0.3 | 0 | 0.3 | 0.3 | 0 | 0.3 | 0.3 | 0
in-channel selectivity | 1.4 | 1.7 | 0.3 | 1.8 | 2.1 | 0.3 | 2.5 | 2.4 | 0.1
adjacent channel selectivity and narrowband blocking | 0 | 0 | 0.3 | 0 | 0 | 0.3 | 0 | 0 | 0.1
in-band blocking | 0 | 0 | 0.3 | 0 | 0 | 0.2 | 0 | 0 | 0.2
receiver intermodulation | 0 | 0 | 0.2 | 0 | 0 | 0.2 | 0 | 0 | 0.1

## Slide 16: Comparison on conducted Vs OTA MU for eAAS and NR FR1 OTA out-of-band blocking requirement
 | Expanded uncertainty ue [dB] |  |  |  |  |  |  |  | 
Wanted signal frequency range: | fwanted ≤ 3GHz |  |  | 3GHz < fwanted ≤ 4.2GHz |  |  | 4.2GHz < fwanted ≤ 6.0GHz |  | 
Interfering signal frequency range: | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU
1MHz < finterferer ≤ 3GHz | 1.3 | 2.0 | 0.7 | 1.5 | 2.0 | 0.5 | 1.9 | 2.0 | 0.1
3GHz < finterferer ≤ 6GHz | 1.5 | 2.1 | 0.6 | 1.7 | 2.1 | 0.4 | 2.0 | 2.1 | 0.1
6GHz < finterferer ≤ 12.75GHz | 3.2 | 3.5 | 0.3 | 3.3 | 3.6 | 0.3 | 3.5 | 3.6 | 0.1

## Slide 17: Way forward on TT for eAAS and NR FR1 OTA out-of-band blocking requirements
 | Test Tolerance [dB] |  |  |  |  |  |  |  | 
Wanted signal frequency range: | fwanted ≤ 3GHz |  |  | 3GHz < fwanted ≤ 4.2GHz |  |  | 4.2GHz < fwanted ≤ 6.0GHz |  | 
Interfering signal frequency range: | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU
1MHz < finterferer ≤ 3GHz | 0 | 0 | 0.7 | 0 | 0 | 0.5 | 0 | 0 | 0.1
3GHz < finterferer ≤ 6GHz | 0 | 0 | 0.6 | 0 | 0 | 0.4 | 0 | 0 | 0.1
6GHz < finterferer ≤ 12.75GHz | 0 | 0 | 0.3 | 0 | 0 | 0.3 | 0 | 0 | 0.1