## Slide 1: Way forward on NR PDCCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20 – 24 August, 2018
R4-1811686

## Slide 2: Agreements
Aggregation levels
  AL2, AL4, AL8
  FFS for AL16
    See page 6 for evaluation of PDCCH AL16 scenario.
Applicability of 4Rx PDCCH demodulation requirements
  Using similar test condition as LTE, 4Rx NR PDCCH demodulation performance tests only if there are continuous PDSCH grants in every slot.
REG Bundle size for 4Rx PDCCH test cases
  Agreement in AH1807: REG bundle size =6 for non-interleaved, 2 for interleaved
  Companies are encouraged to bring evaluation results with both REG bundle size 2 and 6 for 4Rx test cases (case 6,7 and 8) in RAN4#88bis, and decide which value is set based on performance comparison.

## Slide 3: Agreements
Test configurations for 1 symbol PDCCH test case(s)
  Introduce additional requirements with 1 symbol control channel for FR1 FDD with 10MHz and 15kHz SCS (for LTE-NR coexistence scenario)
  See page 5 for the detailed parameters for evaluation
TRS configuration: following same configuration PDSCH demodulation test cases

## Slide 4: Update of simulation assumption
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
1 | 15 | 1_0 | 24 | 39 | 2 | 2 | Non-interleaved | 6 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
2 | 15 | 1_0 | 24 | 39 | 2 | 4 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
3 | 15 | 1_1 | 24 | [50] | 2 | 2 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
4 | 15 | 1_1 | 48 | [50] | 2 | 4 | Non-interleaved | 6 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
5 | 15 | 1_1 | 48 | [50] | 2 | 8 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
6 | 30 | 1_0 | 102 | 41 | 1 | 2 | Interleaved | 2 for 2 Rx [2 or 6 for 4Rx] | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
7 | 30 | 1_1 | 102 | [52] | 1 | 4 | Interleaved | 2 for 2 Rx [2 or 6 for 4Rx] | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
8 | 30 | 1_1 | 102 | [52] | 1 | 8 | Interleaved | 2 for 2 Rx [2 or 6 for 4Rx] | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
9 | 120 | 1_0 | [60] | 41 | 1 | 2 | Interleaved | 2 | [TDL-A, 30ns, 75Hz] | 1x2 Low | NA
10 | 120 | 1_1 | [60] | [51] | 1 | 4 | Interleaved | 2 | [TDL-A, 30ns, 300Hz] | 1x2 Low | NA
11 | 120 | 1_1 | [60] | [51] | 1 | 8 | Interleaved | 2 | [TDL-A, 30ns, 75Hz] | 2x2 Low | NA

## Slide 5: Simulation assumption for 1 symbol PDCCH test case
Companies are encouraged to provide the simulation results in RAN4#88bis to decide the parameters
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
12 | 15 | 1_0 | 48 | 39 | 1 | [4, 8] | Non-interleaved | 6 | [TDL-A, 30ns, 10Hz] | 1x2 Low | 1x4 Low
13 | 15 | 1_1 | 48 | [50] | 1 | [4, 8] | Non-interleaved | 6 | [TDL-A, 30ns, 10Hz] | 1x2 Low | 2x4 Low

## Slide 6: Simulation assumption for PDCCH AL16
Companies are encouraged to provide the simulation results in RAN4#88bis to discuss whether or not to introduce PDCCH AL16 requirements.
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
14 | 15 | 1_0 | 48 | 39 | 2 | 16 | Non-interleaved | 6 | [TDL-A, 30ns, 10Hz] | 1x2 Low | 1x4 Low
15 | 30 | 1_0 | 48 | 41 | 2 | 16 | Non-interleaved | 6 | [TDL-C, 300ns, 100Hz] | 1x2 Low | 1x4 Low
16 | 120 | 1_0 | [60] | 41 | 2 | 16 | Interleaved | 2 | [TDL-A, 30ns, 75Hz] | 2x2 Low | NA