## Slide 1: WF on Evaluation for 2 RX exception in Rel-15 vehicle mounted UE
Volkswagen AG, LG Electronics, Samsung, General Motors, Ericsson, Huawei, Telecom Italia, Vodafone, CMCC
3GPP TSG RAN WG4 Meeting #88
Gothenburg, SE, 20th – 24th Aug, 2018 Agenda Item: 10.3
R4-1811897
(revision of R4-1811840)

## Slide 2: Background (1)
In LS from 5GAA [1], Car OEM requested to allow 2Rx antenna as exceptional case for vehicle mounted NR UE at frequency bands where 4Rx is mandated.
  Use cases are broadband use cases like infotainment or data exchange using Uu interface
  4Rx mandating for some NR operating bands (n7, n38, n41, n77, n78, n79) at FR1 will restrict the design freedom of Car OEM.  need for 2Rx vehicle UE at above listed bands
  If exceptional 2Rx antenna is not agreed, slower deployment of vehicle mounted NR UE is expected which can result in less positive market perception of 5G.
  This exception request is not for the NR V2X service specified in SA1
    This issue is irrelevant with NR V2X study in RAN1.
  RAN4 #87 agreed WF with three candidate options [2]

## Slide 3: Background (2)
RAN plenary agreed to study on evaluation for 2Rx exception in rel-15 vehicle NR mounted UE in RP-181467 with these objectives
  Aspects to study in allowing 2 RX exception for vehicle mounted UEs in frequency bands where 4 Rx is mandated:
    Investigate the impact of 2Rx vehicle mounted UE on coverage and throughput and the possible ways to avoid or at least minimize such impact.
      Link budget with 2 RX vehicular UE
      TCU receiver RF chain and architecture
      Coverage and throughput impacts at system level
    Methods to distinguish vehicular UE from handheld UE
      Methods to define vehicle mounted UEs
      Methods to verify conformance and GCF certification (excluding OTA scope)
LS from 5GAA [3] provided typical antenna gain of vehicle mounted UE.

## Slide 4: Offline Summary
Coverage
  Coverage is more important than throughput: Agreed
    Proposal to remove throughput analysis
  Coverage is based on link budget analysis : Agreed
    Parameters for link budget needs to be agreed in this meeting
  Values of antenna gain from 5GAA LS are used for coverage
    If other prominent antenna mount locations for 2Rx solutions need to be further considered, e.g. 5GAA can provide these
UE type distinction
  UE declaration is enough (OPPO)
    Not enough and Send LS to RAN5/GCF to confirm this (Huawei)
  MIMO layer signaling (LG)
  Additional signaling for UE type? (VDF..)
    Main reason for this is not to allow 2Rx Handheld UE in the network

## Slide 5: WF : Parameters for Coverage
Link budget based analysis will be assumed
  Reference parameters : [4] R4-1809930, Coverage related issues for 2Rx RF requirements of vehicle mounted NR UE as exception case, Samsung
  Parameters in which values need to be changed from [4]
    Antenna Gain + cable loss of device / Body loss / Penetration loss
      Antenna gain + cable loss : Values in 5GAA LS[3] are used in initial analysis
      Body loss : 3dB(ref)  TBD
      Penetration loss : TBD
        Penetration loss includes O2I loss e.g. building/ chassis / ….
  Deployment Scenario
    Hand-held UE(HH)
      4Rx HH outdoor
        Browsing mode
      4Rx HH in-vehicle
        Dashboard / Passenger Holding in browsing mode
        Charger position can be considered by interested company
    Vehicle mounted UE(V)
      2Rx V outdoor
        Antenna gains and cable loss will be used for the roof and other typical locations
  Reference bands
    Either n7 or n41

## Slide 6: WF : Throughput
RAN4 agreed throughput is out-of-scope of RAN4 WG
  This will be further discussed in RAN plenary

## Slide 7: WF: Methods to distinguish UE type
Problem statement:
  Description/clarification of the reasons for the need for declaration of the UE type:
    Conformance tests, certification tests, network operation/optimization reasons etc.
Solution based on the problem statement :
  Development of a solution/method to distinguish the UE type
  Clarification of the involvement of other groups (RAN2 : adding signaling issues in rel-15)
    Signaling option can be considered when the necessity of this signaling is clearly understood in NW perspective.
Options to distinguish UE type :
  Option 1: No signalling
    UE shall make declaration
  Option 2: Signalling
    2-1 : use MIMO layer signalling (defined the UE capability signalling as optional feature in NR)
    2-2 : New signalling

## Slide 8: WF : Schedule/Roadmap
RAN4 #88
  High level agreement on
    Coverage related assumption
      Antenna gain
    UE type distinction
      Potential options among Option 1 and 2
RAN4 #88Bis
  Initial calculation on coverage
  Review of the requested antenna data, in-vehicle positions, penetration loss
  Decision on the measures for the 2Rx exception
  Complete UE type distinction method
    Decision on the necessity of new signaling
    If yes, send LS to RAN2 on RAN4 decision
RAN4 #89
  Complete evaluation for coverage
  LS to RAN Plenary on the conclusion

## Slide 9: References
[1] R4-1806142, LS from 5GAA on minimum number of RX antennae for NR vehicular UEs
[2]R4-1808169 WF on 2Rx requirements for vehicle mounted NR UE, LG Electronics
[3] R4-1811528, LS from 5GAA for rel-15 2 RX vehicle mounted UE
[4] R4-1809930, Coverage related issues for 2Rx RF requirements of vehicle mounted NR UE as exception case, Samsung
[5] RP-181117, Minimum requirement of 2Rx antennas for permanently mounted UE in vehicles for NR, Volkswagen AG
[6] TR38.901