## Slide 1: WF for NR PUSCH demodulation
Nokia, Nokia Shanghai Bell, […]
R4-1813214
Document for: Approval
3GPP TSG-RAN WG4 RAN#88bis
Chengdu, China, 8 – 12 October, 2018
Agenda: 7.13.2.2

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809336, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88

## Slide 3: Time domain resource
For FR1,
  Agreement on Monday
    FFS: whether to test slot-based transmission with resource mapping type B
      Discuss the feasbility to define one set performance requirements for FR1 slot-based transmission for both PUSCH mapping type A and B.
    FFS: Whether to test non-slot based transmission with resource mapping type B
    Discuss further offline in this week.
  Discussion on Tuesday
    Compromise proposal (Nokia)
      We agreed to test slot-based with mapping A.
      Can we then agree on testing non-slot based with mapping B?
        Agree: Nokia, Ericsson, ZTE, China Telecom, Samsung
        Against: Huawei
    Competing compromise (Huawei)
      Type B for both slot and non-slot based.
For FR2
  Number of UL symbols: 10
  Start symbol index: 0

## Slide 4: Frequency domain resource
Frequency domain resource for DFT-s-OFDM:
  Simulate the following by the next meeting
    Based on results, it will be decided if one SCS/BW combination is sufficient per FR in the next meeting.
    Check the PRB number of 30 in this week.
SCS | BW in PRB | BW in MHz
15 (FR1) | 25 | 5
30 (FR1) | 24 | 10
60 (FR2) | [30] in the middle of the channel BW | 50
120 (FR2) | [30] in the middle of the channel BW | 100

## Slide 5: DMRS configuration
EPRE ratio of PUSCH to DM-RS for DMRS type 1
  -3dB
Additional DMRS for DFT-S-OFDM
  The same configuration with CP-OFDM
Discussion on Tuesday
  DMRS for CP-OFDM
    For FR2
      Option 1: 1+0 and 1+1
      Option 2: 1+0

## Slide 6: UCI on PUSCH
Specify test cases for UCI decoding performance over PUSCH in Rel-15 by Next June
Test parameters to be discussed after the Nov meeting.

## Slide 7: Reference receiver and MIMO correlation for 2Tx PUSCH
Reference receiver and MIMO correlation for 2Tx PUSCH
  Reference receiver for 2Tx PUSCH
    MMSE receiver
  MIMO correlation: low

## Slide 8: PTRS configuration
PTRS configuration
  Frequency density KPTRS for CP-OFDM:
    2
Discussion on Tuesday
  Default thresholds for PT-RS patterns for DFT-S-OFDM
    NRB0=0, NRB1=8, NRB2=NRB3=32, and NRB4=108
  Support : Ericsson, CATT, ZTE
  Huawei want to further check in this meeting