## Slide 1: Way forward on NR UE CSI requirements
Samsung
3GPP TSG-RAN WG4 Meeting RAN4#88bis R4-18xxxxx
Chengdu, China, 8-12 Oct, 2018

## Slide 2: Previous agreed test cases list
Static CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband fading CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband PMI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 8*2, 8*4
  Test 2: FR1 TDD 40MHz&30kHz, 8*2, 8*4
  Test 3: FR2 100MHz& 120kHz, 2*2
  Test 4: FR1 FDD 10MHz &15kHz , 4*2, 4*4
  Test 5: FR1 TDD 40MHz&30kHz, 4*2, 4*4
RI test
  Test 1: FR1 FDD 10MHz&15kHz, 2*2,4*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 4*4
  Test 3: FR2 100MHz&120kHz, 2*2
Sub-band CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4

## Slide 3: Test Set-up (1/2)
Skip scheduling PDSCH in CSI-RS and special sub-frames during CSI test cases
NZP CSI-RS configurations
ZP CSI-RS configurations
CSI-IM configurations
First subcarrier index in the PRB used for CSI-RS (k0, k1) | Row 3, (6,-) | Row 54,(0,-) | Row 8,(4,6)
First OFDM symbol in the PRB used for CSI-RS (l0) | 513 | 513 | 5
Number of CSI-RS ports (X) | 2 | 4 | 8
CDM Type | FD-CDM2 | FD-CDM2 | CDM4 (FD2,TD2)
Density (ρ) | 1 | 1 | 1
Parameters | FR1 | FR2
CSI-IM-RE-pattern | Pattern 0 | Pattern 1
CSI-IM-ResourceMapping (kCSI-IM,lCSI-IM) | (4,9) | (8,913)
Parameters | FR1 | FR1FR2
First subcarrier index in the PRB used for CSI-RS (k0) | Row 5, 4 | Row 4, 8
First OFDM symbol in the PRB used for CSI-RS (l0) | 9 | 913
Number of CSI-RS ports (X) | 4 | 4
CDM Type | FD-CDM2 | FD-CDM2
Density (ρ) | 1 | 1

## Slide 4: Test Set-up (2/2)
CSI-RS resource/CSI reporting periodicity slot offset for periodic CSI reporting
  FR1 FDD 15kHz: 5/1
  FR1 TDD 30kHz:
    Option 1: 10/1
  FR2 TDD 120kHz:
    Option 1: 16/1
    Option 2: 8/1
  Minimum CSI delay for periodic CSI: 8ms
CSI-RS resource/CSI reporting interval and slot offset for aperiodic CSI reporting
  FR1 FDD 15kHz: 3/1 with total CSI delay 6 slots
  FR1 TDD 30kHz: 5/1 with total CSI delay 10 slots
  FR2 TDD 120kHz: 12/1 with total CSI delay 24 slots
CSI reporting and CSI-RS resources Type for fading CQI test cases and RI test cases of FR2
  Option 1: Periodic (previous meeting agreements)
  Option 2: aperiodic (baseline)
  Companies are encouraged to bring analysis for above options considering different CSI delay assumptions for periodic and aperiodic CSI reporting types
Number of HARQ process number
  FR1 FDD:4
  FR1 TDD: 8
  FR2 TDD:
    Option 1:8
    Option 2:10

## Slide 5: Static CQI test cases
Test metric
  Static CQI:
    The reported CQI value shall be in the range of ±1 of the reported median more than 90% of the time.
    If the PDSCH BLER using the transport format indicated by median CQI is less than or equal to 0.1, the BLER using the transport format indicated by the (median CQI + 1) shall be greater than 0.1. If the PDSCH BLER using the transport format indicated by the median CQI is greater than 0.1, the BLER using transport format indicated by (median CQI – 1) shall be less than or equal to 0.1.
Rank: Rank2 with codebook restriction 010000
Test SNR points:
  Option 1:
    FR1 2Rx:[8/9]dB, [14/15]dB
    FR1 4Rx:[5/6]dB, [11/12]dB
    FR2 2Rx:[8/9]dB, [14/15]dB
  Other options not excluded
  Companies are encouraged to bring evaluation results to decide test SNR points in RAN#89 meeting

## Slide 6: Wideband fading CQI test cases
Test metric
  a) a CQI index not in the set {median CQI -1, median CQI, median CQI +1} shall be reported at least a % of the time;
  b) the ratio of the throughput obtained when transmitting the transport format indicated by each reported wideband CQI index and that obtained when transmitting a fixed transport format configured according to the wideband CQI median shall be ≥ g ;
  c) when transmitting the transport format indicated by each reported wideband CQI index, the average BLER for the indicated transport formats shall be greater or equal to TBD.
Rank : Rank1 with codebook restriction: 000001
Test SNR points:
  Option 1:
    For FR1 2Rx (FDD and TDD): 6/7dB +12/13 dB
    For FR1 4Rx (FDD and TDD): 3/4dB +9/10 dB
    For FR2 2Rx (TDD): 6/7dB +12/13 dB
  Other options not excluded
Companies are encouraged to bring results among 0 dB~20 dB with 2dB step size
  Relative throughput ratio between following CQI and median CQI , BLER with following CQI, reporting CQI percentile out side of {median CQI-1 ~median CQI +1}
Test SNR points and corresponding requirements will be decided in RAN4#89 based on companies’ evaluation results

## Slide 7: Sub-band CQI Test cases
Introduce sub-band CQI test cases in FR1 only
Test metric
  a) a sub-band differential CQI offset level of 0 shall be reported at least a % of the time but less than b % for each sub-band;
  b) the ratio of the throughput obtained when transmitting on a randomly selected sub-band among the sub-bands with the highest differential CQI offset level the corresponding TBS and that obtained when transmitting the TBS indicated by the reported wideband CQI median on a randomly selected sub-band in set S shall be ≥ g;
  c) when transmitting on a randomly selected sub-band among the sub-bands with the highest differential CQI offset level the corresponding TBS, the average BLER for the indicated transport formats shall be greater or equal to TBD.
Test SNR points:
  FFS between [0~20] dB
  Companies are encouraged to bring results within [0~20]dB with 2dB step size
Channel model and MIMO correlation:
  FR1: (MIMO correlation mode using 36.101 B.1 model)
  Rank : Rank 1 with codebook restriction: 000001
    Option 1: 2*2, 2*4 (baseline)
    Option2: 1*2, 1*4
  Channel Model：Clause B.2.4 in TS 36.101, with a =1
    FR1 FDD 10MHz： fD =5Hz
    FR1 TDD 40MHz： , fD =10Hz
  CSI-RS resources and CSI reporting Type: Periodic
  Sub-band size:
  FR1 FDD 10MHz: 8 RBs
  FR1 TDD 40MHz: 16 RBs
Companies are encouraged to bring results :
  Relative throughput ratio between following CQI on selected sub-band and median wideband CQI on a random selected sub-band with full size
  BLER with following CQI on selected sub-band
  The percentile of reported sub-band differential CQI offset level equals to 0 for each sub-band with full size

## Slide 8: PMI test cases
Test metric: Reusing LTE test metric
  Relative Throughput ratio between following PMI and random PMI at SNR point corresponding to X% TP with follow PMI.
    Option 1: X = 70 (previous agreement)
    Option 2: X= 90
Test requirements
  Companies are encouraged to bring results to decide test requirements in RAN4#89
MCS and Rank for FR2 2Tx PMI test case:
  Option 1:MCS 13 and Rank1 (baseline)
  Option 2: MCS 4 and rank1
MIMO correlation for FR2 2Tx PMI test case:
  Option 1: ULA Low
  Option 2: ULA medium
  Option 3: XP Medium A

## Slide 9: RI test cases
Test metric:
  a) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 1 shall be ≥ g1;
  b) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 2 shall be ≥ g2;
MIMO correlation:
  FR1 TDD: TDL_A 30ns, 10Hz, ULA Low and ULA High
  FR1 FDD: TDL_A 30ns, 5Hz,ULA Low and ULA High
  FR2 TDD: TDL-A 30 ns, 75 Hz for FR2 TDD,ULA Low, XP Medium XP High
For simulation purpose, companies are encouraged to provide following Rank, fixed rank1 and fixed rank2 results among -6dB ~30dB with 2 step size
  For RI test cases with 4Tx 4Rx, interested companies can bring the simulation results for fixed rank 3 and rank 4 should also be collected, in order to help decide the final test metric.
TxRx:
  2Rx: 2Tx
  4Rx: 2Tx and 4Tx
Codebook restriction: (base line, other options not excluded)
  2Tx
    000011 for fixed RI = 1
    010000 for fixed RI = 2
    010011 for UE reported RI
  4Tx
    11111111 with N1 =2, N2 =1
Test points (starting point): (further discussed for the test points, SNR and corresponding requirements)
  2Rx
  4Rx
Test Number | Test 1 (2X2) | Test 2 (2X2) | Test 3 (2X2)
MIMO correlation | ULA Low | ULA Low | ULA High for FR1 XP Medium for FR2
Metric | Gamma 2 | Gamma 1 | Gamma 1
SNR | FFS (Low) | FFS (High) | FFS (High)
Test Number | Test 1 (2X4) | Test 2 (2X4) | Test 3 (2X4) | Test 4 (4X4)
MIMO correlation | ULA Low | ULA Low | ULA High | ULA Low
Metric | Gamma 2 | Gamma 1 | Gamma 1 | Gamma 2
SNR | FFS (Low) | FFS (medium) | FFS (medium) | FFS (High)