## Slide 1: WF for NR PUSCH demodulation
Nokia, Nokia Shanghai Bell, […]
R4-1813942
Document for: Approval
3GPP TSG-RAN WG4 RAN#88bis
Chengdu, China, 8 – 12 October, 2018
Agenda: 7.13.2.2

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88

## Slide 3: Time domain resource
For FR1,
  Whether to test non-slot and/or slot based transmission with resource mapping type B
    Option1: Type B for non-slot based.
    Option2: Type B for slot based
    Option3: Type B for both slot and non-slot based.
    Option4: Type B not tested
For FR2
  Number of UL symbols: 10
  Start symbol index: 0

## Slide 4: Frequency domain resource
Frequency domain resource for DFT-s-OFDM:
  Simulate the following by the next meeting
    Based on results, it will be decided if one SCS/BW combination is sufficient per FR in the next meeting.
SCS | BW in PRB | BW in MHz
15 (FR1) | 25 | 5
30 (FR1) | 24 | 10
60 (FR2) | 30 in the middle of the channel BW | 50
120 (FR2) | 30 in the middle of the channel BW | 100

## Slide 5: DMRS configuration
EPRE ratio of PUSCH to DM-RS for DMRS type 1
  -3dB
Additional DMRS for DFT-S-OFDM
  The same configuration with CP-OFDM

## Slide 6: UCI on PUSCH
Specify test cases for UCI decoding performance over PUSCH in Rel-15 by Next June
Test parameters to be discussed after the Nov meeting.

## Slide 7: Reference receiver and MIMO correlation for PUSCH
Reference receiver and MIMO correlation for PUSCH
  Reference receiver for 2Tx PUSCH
    MMSE receiver
  MIMO correlation: low

## Slide 8: PTRS configuration
PTRS configuration
  Frequency density KPTRS for CP-OFDM:
    2
  Default thresholds for PT-RS patterns for DFT-S-OFDM
    NRB0=0, NRB1=8, NRB2=NRB3=32, and NRB4=108

## Slide 9: Initial simulation assumptions, CP-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1, 2 | 1, 2
Number of Rx | 2, 4, 8 | 1, 2
Number of layers | 1, 2 | 1, 2
Transmission scheme | Identity matrix (TPMI index 0) | Identity matrix (TPMI index 0)
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A | type B
Frequency domain resource | full RB allocation of the applicable BW | full RB allocation of the applicable BW
MCS index | 2, 16, 20 (20 only for 1Tx) | 2, 16, 20 (20 only for 1Tx)
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | [TDL]
SCS and BW | To be captured in work plan WF | 
PTRS | Not configured | Configured with KPTRS =2, LPTRS =1
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group | Disabled | Disabled
Frequency hopping | Disabled | Disabled
Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput
Notes: Nokia Remarks on sources:
  Reduction of the combinations to simulate can be done in the work plan WF.
  Number of layers = 1,2 in FR1 is captured in R4-1809370
  Number of layers = 1,2 in FR2 is captured in R4-1809366
  2, 16, 20 (20 only for 1Tx) is captured in R4-1809366
  [TDL] from BS demod Adhoc Minutes RAN4-88b

## Slide 10: Initial simulation assumptions, DFT-S-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | enabled | enabled
Number of Tx | 1 | 1
Number of Rx | 2, 4, 8 | 1, 2
Number of layers | 1 | 1
DMRS type | type 1 | Type 1
Number of DMRS symbols | 1+1, 1 | 1
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A | type B
Frequency domain resource | 15kHz: 25 PRB (contig., middle of test BW) 30kHz: 24 PRB (contig., middle of test BW) | 60kHz: 30 PRB (contig., middle of test BW) 120kHz: 30 PRB (contig., middle of test BW)
MCS index | 2 | 2
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | [TDL]
SCS and BW | 15kHz: 5 MHz 30kHz: 10 MHz | 60kHz: 50 120kHz: 100
PTRS | Not configured | NRB0=0, NRB1=8, NRB2=NRB3=32, and NRB4=108
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group | Disabled | Disabled
Frequency hopping | Disabled | Disabled
Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput
Notes: Nokia Remarks on sources:
  MCS = 2 (only) is captured in R4-1811694