## Slide 1: Way forward on RRM test setup for R15 V2X CA
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #88bis Chengdu, China, 8th – 12th October, 2018
Agenda item: 6.3.4
R4-1814038

## Slide 2: Agreements on R15 V2X Synchronization Reference Source selection/reselection Test
To define the test for GNSS configured as highest priority
Test principles are proposed as follows:
  The test includes three time period, T1, T2 and T3. PCell is only detectable on RF channel 3 during T1. SyncRef UE 1 is only detectable on RF channel 1 during T3. There is no detectable SyncRef UE on RF channel 2 during whole test.
  During T1, two V2X CCs (RF channel 1 and RF channel 2) are aggregated for V2X sidelink communications, and both of these two CCs are also configured as synchronous carriers. UE select Pcell as synchronous source.
  During T2, PCell is power off, and no SyncRef UE is detected.
  During T3, UE will identify SyncRef UE 1 on RF channel 1 and select SyncRef UE 1 as synchronous source.

## Slide 3: Agreements on R15 V2X Interruption Test
Only the interruptions on WAN due to V2X CC addition based on dedicated RRC signaling will be verified.
Further study the number of missing ACK/NACKs due to the interruptions in RRM test.
  Further study whether to define separate test for Uu FDD and Uu TDD cases.
  If the number of missing ACK/NACKs are same for both FDD and TDD, the interruption test can be defined only for one case.
Define the test with asynchronous scenario between downlink and sidelink.