## Slide 1: WF on Clarification on LAA channel access for multi-carrier operation
Ericsson, Nokia, T-Mobile Inc, Charter, CableLabs, US Cellular, …
R4-1814100
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8-12 October 2018
Agenda Item: 4.2.2.1

## Slide 2: Background
Following contributions are submitted in RAN4#88bis on LAA channel access for DL multi-carrier operations:
  R4-1812321: Further analysis and new proposal to address co-existence of Wi-Fi and certain LAA multi-carrier combinations, Charter Communications, Inc
  R4-1813332: Regarding band 46 intra-band LAA combinations involving 4 or less carriers, Ericsson
  R4-1813395: Clarification on LAA channel access, Nokia, Nokia Shanghai Bell, T-Mobile US

## Slide 3: Agreements: Choose one of the options
Option 1
  Apply channel bonding for DL in Rel-13 similar to UL in Rel-14
Option 2
  Apply DL channel bonding from Rel-15 onwards
  Prohibit non-contiguous intra-band CA in band 46 in Rel-13 and Rel-14 which violates the following:
    The maximum frequency separation between the two outermost carriers shall be less than 62MHz
    This will be specified in TS 36.307
Option 3
  For maximum frequency separation between the center frequencies of the any two carriers on which LAA transmissions are performed is <=62MHz, do not apply DL Wi-Fi channel bonding.
  For maximum frequency separation between the center frequencies of the any two carriers on which LAA transmissions are performed is >62MHz, apply DL Wi-Fi channel bonding from Rel’13 , for all combinations part of the channel superset see slide #4).
    Allow Type B LBT on each set of carriers that does not include any carrier frequencies that are included in any of the sets of EARFCN for carriers which are part of the Wi-Fi model (see slide 4)
    The above also means that, non-contiguous intra-band CA (with maximum frequency separation between the center frequencies of the any two carriers on which LAA transmissions are performed is >62MHz) in band 46 are allowed from Rel-13, provided that the above conditions are met.
Option 4
  For maximum frequency separation between the center frequencies of the any two carriers on which LAA transmissions are performed is <=62MHz, apply DL Wi-Fi channel bonding for Rel 15 and onwards
  For maximum frequency separation between the center frequencies of the any two carriers on which LAA transmissions are performed is >62MHz, apply DL Wi-Fi channel bonding from Rel’13 , for all combinations part of the channel superset see slide #4).
    Allow Type B LBT on each set of carriers that does not include any carrier frequencies that are included in any of the sets of EARFCN for carriers which are part of the Wi-Fi model (see slide 4)
    The above also means that, non-contiguous intra-band CA (with maximum frequency separation between the center frequencies of the any two carriers on which LAA transmissions are performed is >62MHz) in band 46 are allowed from Rel-13, provided that the above conditions are met.

## Slide 4: Super Set Options
Option 1 (FCC case)
  for sets of two Scells: n-2, n-1, n, n+1, n+2 | n = {47090, 47290}, {47490, 47690}, {47890, 48090}, {48290, 48490}, {50290, 50490}, {50690, 50890}, {51090, 51290}, {51490, 51690}, {51890, 52090}; {52290, 52490}; {52740, 52940}; {53140, 53340}
  for sets of four Scells: n-2, n-1, n, n+1, n+2 | n = {47090, 47290, 47490, 47690}, {47890, 48090, 48290, 48490}, {50290, 50490, 50690, 50890}, {51090, 51290, 51490, 51690}, {51890, 52090, 52290, 52490}, {52740, 52940, 53140, 53340}
  for sets of eight Scells: n-2, n-1, n, n+1, n+2 | n = {47090, 47290, 47490, 47690, 47890, 48090, 48290, 48490}, {50290, 50490, 50690, 50890, 51090, 51290, 51490, 51690}
Option 2 (ETSI)
  for sets of two Scells: n-2, n-1, n, n+1, n+2 | n = {47090, 47290}, {47490, 47690}, {47890, 48090}, {48290, 48490}, {50290, 50490}, {50690, 50890}, {51090, 51290}, {51490, 51690}, {51890, 52090}
  for sets of four Scells: n-2, n-1, n, n+1, n+2 | n = {47090, 47290, 47490, 47690}, {47890, 48090, 48290, 48490}, {50290, 50490, 50690, 50890}, {51090, 51290, 51490, 51690}
  for sets of eight Scells: n-2, n-1, n, n+1, n+2 | n = {47090, 47290, 47490, 47690, 47890, 48090, 48290, 48490}, {50290, 50490, 50690, 50890, 51090, 51290, 51490, 51690}
Combination of option 1 and option 2 are not precluded.
Channel 0 (5160MHz), 9 (5340MHz), 16 (5480MHz) of ETSI set need further consideration.

## Slide 5: Additional Agreements
No changes are required in TS 36.141
Time plan:
  Agree on CRs in RAN4#89.