## Slide 1: WF on 2 Rx vehicle UE: Link budget simulation assumptions
SAMSUNG, LG Electronics, Volkswagens AG
3GPP TSG-RAN WG4#88bis Meeting
Chengdu, China, 08-12 Oct. 2018 Agenda Item: 10.3
R4-1814143

## Slide 2: Offline Discussion Results 1. Coverage analysis and Link budget simulation assumptions

## Slide 3: Agreement 1: WF on Parameter for Link Budget Evaluation
 |  | 4Rx HHUE (Outdoor browsing) | 4Rx HHUE (Passenger Holding browsing) | 4Rx HHUE (Dash board) | 2Rx VUE
Antenna Configuration |  | 4Rx/2Tx | 4Rx/2Tx | 4Rx/2Tx | 2Rx/2Tx
BS Antanna Gain1 [dBi] |  | 18 | 18 | 18 | 18
UE Antenna Gain | Antenna system gain per element 2,5 [dBi] | -7.5 | -7.5 | -4.5 | -3
 | Penetration Loss3 [dB] | 0 | 9 | 9 | 0
 | Total [dB] | -9.5 | -18.5 | -15.5 | -3
Fading Margin [dB] |  | [9] | [9] | [9] | [9]
Interference Margin [dB] |  | 3 | [3] | [3] | 3
DL | BS Tx Power [dBm] | 46 | 46 | 46 | 46
 | UE REFSENS4 [dBm] | -87.4 | -87.4 | -87.4 | -84.7
Note 1. E/// proposed during AH. Note 2. Antenna system gain per element = (ant. efficiency + directivity) + cable/Body Loss Note 3. O2I car penetration loss is based on TR38.901 7.4.3.2 Note 4. 4 Rx REFSENS = 2 Rx REFSENS (TS38.101-1 Table 7.3.2-1) + ΔRIB,4R (TS38.101-1 Table 7.3.2-2) Note 5: To be confirmed by feedback from 5GAA on definition of the term ‘baseline’ for vehicle antenna performance |  |  |  |  | 

## Slide 4: Agreement 2: Conclusion on parameters for Link Budget Evaluation
In RAN 4 #88bis, -3dBi is initially used for vehicle UE antenna gain (as provided by 5GAA LS). Conclusion of RAN 4 study is subject to:
Provision of antenna system gain per element by means of TRP* measurements (with no stringent time budget, if possible RAN #82, per note 2) by OEMs in 3GPP or 5GAA
TRP is used to infer gain of the system, although receiver link budgets are discussed
In note 2: Detailed values for n7/n41 are based on follows:
HH-UE : https://www.gsma.com/newsroom/wp-content/uploads/TS-24-v3-01.pdf
Vehicle UE : 5GAA LS (R4-1811528)