## Slide 1: 3GPP TSG-RAN WG4 Meeting #90bis Xi’An, China, 8th – 12th April 2019
Huawei, HiSilicon
Way forward on RRM for Rel-16 eMTC
R4-1903796

## Slide 2: DL quality report
MPDCCH parameter for DL quality report in Msg3 is re-used from RLM, expect maximal repetition level and aggregation level.
  If the repetition number in DL quality information is larger than 1, the MPDCCH aggregation level is 24.
  If the repetition number in DL quality information equals to 1, wait for RAN1 decision to determine the maximal MPDCCH repetition level and aggregation level.
Re-use the same evaluation period (T1 and T2) from NB-IoT for eMTC for DL quality report in Msg3.
The definition of measurement accuracy of DL quality report in Msg3 can re-use from NB-IoT.
RAN4 to discuss the report mapping and accuracy requirements for DL quality report in Msg3 after RAN1 makes agreements on the number of bits and contents of the report.
RAN4 to wait for more RAN1/2 conclusions on DL quality report in connected mode before discussing the RRM impact.

## Slide 3: WUS
In Rel-16, Rel-15 WUS reception requirements apply for Rel-15 UE.
RAN4 to check if Rel-15 WUS reception requirements can apply for Rel-16 UE when Rel-15 WUS is sharing same WUS resource with Rel-16 WUS with single-sequence CDM.
RAN4 to check if new requirements for needed for Rel-16 WUS reception based on the sequence design, for shared and not-shared WUS resource.

## Slide 4: PUR
RAN4 does not need to define RRM requirements for TA validation based on serving cell change.
RAN4 does not need to define the threshold for time duration for TA validation. The TA timer is up to network configuration.
RAN4 does not need to define the threshold for TA change or DL/UL timing change. It is expected that network will configure proper RSRP threshold based on UE’s original TA.

## Slide 5: Relaxed serving cell monitoring
The serving cell monitoring relaxation defined for Rel-15 NB-IoT is used for eMTC
  The condition for enabling relaxed serving cell monitoring is directly re-used from NB-IoT.
  The relaxation factor for eMTC can be defined in the same way as NB-IoT by replacing DRX cycle length {1.28, 2.56, 5.12, 10.24} with {0.32, 0.64, 1.28, 2.56}.
  Same time period of T0 as in NB-IoT is introduced where relaxed serving cell monitoring is not allowed.