## Slide 1: WF on nominal channel spacing
ZTE, [...]
3GPP TSG-RAN WG4 #90bis Meeting
Xi'an, China, 8th - 12th Apr. 2019
R4-1905133

## Slide 2: Background (1)
For intra-band contiguously aggregated carriers, the channel spacing between adjacent component carriers shall be multiple of least common multiple of channel raster and sub-carrier spacing.
The nominal channel spacing between two adjacent aggregated NR carriers is defined as follows:
For NR operating bands with 100 kHz channel raster:
For NR operating bands with 15 kHz channel raster:
with
For NR operating bands with 60kHz channel raster:
with

## Slide 3: Background (2)
The channel spacing for intra-band contiguous carrier aggregation can be adjusted to any multiple of least common multiple of channel raster and sub-carrier spacing less than the nominal channel spacing to optimize performance in a particular deployment scenario.
Channel spacing is fixed when SCS changes.
For intra-band contiguous CA, the guard band of the two outermost carriers are symmetrical from UE aspect.
Some RF requirements are based on aggregated channel bandwidth, such as Tx ON/OFF power, OBW, etc.
In current specs, no RF requirements are defined in the gap between carriers for intra-band contiguous CA.

## Slide 4: Potential issue (1)
  For intra-band contiguous CA, CC1 and CC2 with differernt SCS configurations, the nominal channel spacing may vary when SCS changes, leading to ambiguity on being contiguous or non-contiguous for the same placement.
  Carrier spacing may be wider than the nominal channel spacing for a certain SCS configuration, which can be seen as intra-band non-contiguous CA according to the current descriptions in the spec.
nominal channel spacing
nominal channel spacing
15kHz SCS
15kHz SCS
30kHz SCS
30kHz SCS
nominal channel spacing
60kHz SCS
60kHz SCS

## Slide 5: Potential issue (2)
  Ambiguity on being contiguous or non-contiguous for each combinations of CC1(SCSx) and CC2(SCSy) according to the current RAN4 specs with the above configurations as one example:
    CC1 (SCS1) and CC2(SCS1) : continguous or non-contiguous?
    CC1 (SCS1) and CC2(SCS2) : continguous or non-contiguous?
    CC1 (SCS2) and CC2(SCS1) : continguous or non-contiguous?
    CC1 (SCS2) and CC2(SCS2) : continguous or non-contiguous?
carrierBandwidth1, SCS1
carrierBandwidth BW2, SCS2
carrierBandwidth1, SCS1
carrierBandwidth BW2, SCS2
CC#1 (SCS1)
CC#2 (SCS1)
CC#1 (SCS2)
CC#2 (SCS2)

## Slide 6
carrierBandwidth1, SCS1
carrierBandwidth BW2, SCS2
Scenario 1
Reference Channel bandwidth(BW1)
Reference Channel bandwidth(BW2)
carrierBandwidth BW1, SCS1
carrierBandwidth BW2, SCS2
Scenario 2
carrierBandwidth BW1, SCS1
carrierBandwidth BW2, SCS2
carrierBandwidthBW1, SCS1
carrierBandwidthBW2, SCS2
Scenario 3
Scenario 4
carrierBandwidth1, SCS1
carrierBandwidth BW2, SCS2
Scenario 1
carrierBandwidth BW1, SCS1
carrierBandwidth BW2, SCS2
Scenario 2
carrierBandwidth BW1, SCS1
carrierBandwidth BW2, SCS2
carrierBandwidthBW1, SCS1
carrierBandwidthBW2, SCS2
Scenario 3
Scenario 4
Min. GB

## Slide 7
Specify that BW1 and BW2 as reference channel bandwidth in the calculation of nominal channel spacing
  Reference channel bandwidth means the frequency span in MHz from the defined tables in RAN4 specs, covering all of the supported SCSSpecific-Carrier. Scenarios that carrier bandwidth with different SCSs can be fully overlapped
  Terminology “Reference channel bandwidth” will not be used in the specs texts, only for the convenience of discussion
Agreement

## Slide 8
Further check difference between UE and BS reference channel bandwidth
Further check SCS corresponding to the reference channel bandwidth (reference SCS) if guard-band keeps in the equations calculating the nominal channel bandwidth
Potential specs change should minimize the impact on the channel spacing
Agreement (Cont’d)

## Slide 9: Reference
R4-1902870 Nominal Channel Spacing for CA for FR1 and FR2, Intel
R4-1903832 Discussion on the Nominal channel spacing for CA, ZTE Corporation
R4-1903949 On the carrier frequency mapping and CA channel spacing, Ericsson
R4-1904164 Views on nominal channel spacing for CA, NTT DOCOMO
R4-1904269 Nominal channel spacing for CA and definition of contiguous/non-contiguous CA, Nokia