## Slide 1: 3GPP TSG-RAN WG4 Meeting #91 Reno, United States of America, 13 – 17 May, 2019
Ericsson
Way forward on Rel-16 MTC RRM enhancement
R4-1906794

## Slide 2: Preconfigured UL resource
When TA validation based on serving cell RSRP change method is configured, eNodeB shall determine and configure a single RSRP threshold to the UE.
Relaxed serving cell monitoring shall not be allowed when the UE is configured with TA validation method using serving cell RSRP change for PUR.

## Slide 3: Mobility enhancement
RSS based RSRP measurement is used in random access procedure for improving the CE level selection when multiple CE levels are configured if improved measurement accuracy can be achieved using RSS compared CRS.
RAN4 shall discuss whether RSS can be used for improving the neighbor cell procedures (e.g. measurements) once progress on RSS signaling work is made in other WGs.