## Slide 1
3GPP TSG-RAN WG4 Meeting #92 R4-1908680
Ljubljana, SI, 26th– 30th August, 2019
Agenda Item: 9.16.2
WF on demodulation for NR HST
CMCC

## Slide 2: Agreements
3.6GHz with 500km/h is considered in R16 NR HST
  the DL maximum Doppler shift is 1.7 KHz
  the UL maximum Doppler shift is 3.4 KHz

## Slide 3: Agreements
For UE demodulation, it is proposed to consider following channel models:
  HST-SFN with bidirectional coverage
  HST single tap
  multi-path fading channel
For HST-SFN deployment, following two transmission scheme are considered for UE demodulation:
  HST-SFN with joint transmission
    the channel model defined in Section B.3A of 3GPP TS 36.101 can be used as a baseline. And the parameters, e.g. Ds, Dmin, may be different based on NR deployment.
  HST-SFN with DPS transmission
  To support working at 3.6GHz with 500km/h, following UE demodulation requirements need to be specified:
  PDSCH
  Other requirements are not precluded if needed

## Slide 4: Agreements
For BS demodulation, BS vendor’s inputs are encouraged to determine the channel model between following two options:
  Option 1: HST single tap, the time/frequency tracking and demodulation are performed by each RRH
  Option 2: HST-SFN, the time/frequency tracking and demodulation are performed by BBU
  To support working at 3.6GHz with 500km/h, following BS demodulation requirements need to be specified:
  PUSCH
  PRACH
    PRACH Format 3/Ax/Bx/Cx are considered
  Other requirements are not precluded if needed