## Slide 1: WF on the NR-U channel raster
Ericsson,
3GPP TSG-RAN4 Meeting #92 R4-1909395 Ljubljana, slovenia, 26-30 Aug, 2019

## Slide 2: Background
According to chairman note:
  Companies will continue discuss on the down-selection scheme for channel raster based on the non co-existence scenarios and co-existence scenarios with WiFi channel
This slide propose the possible WF on channel raster design on NR-U on 5GHz band (n46)

## Slide 3: Proposal
Scenario: non coexisting with wifi, LAA
  Down selection Nref is Based on R15 NR channel raster of 15kHz granularity (Table 5.4.2.1-1 in 38.104 for frequency range 3000MHz – 24250 MHz), for different SCS of the same BW, the step size of Nref will be adjusted accordingly (i.e for SCS = 15kHz, step size =1; for SCS=30kHz, step size = 2, for SCS=60kHz, step size = 4）
  need further confirmation on RAN1 spec impact
    Impact on required SSB-CORESET0 offset values
    For standalone deployment, impact on UE assumption on time/frequency resources to monitor for reception of SIB1
  Further confirmation on possibility of the guarantee of scenario of non coexistence with wifi
  Further confirmation with RAN1 with common understanding on WID scope of considering non coexisting scenario with Wifi
Prioritized Scenario : co-existing with wifi, LAA in R16
  Down selection principle:
    Down selection Nref is Based on R15 NR channel raster of 15kHz granularity (Table 5.4.2.1-1 in 38.104 for frequency range 3000MHz – 24250 MHz), for different SCS of the same BW, the step size of Nref will be adjusted accordingly (i.e for SCS = 15kHz, step size =1; for SCS=30kHz, step size = 2 , for SCS=60kHz, step size = 4)
    For 20 MHz BW: Select NREF with its corresponding RF reference frequency (FREF) as close as to the WIFI nominal center frequency. Two more center frequency on 5885MHz and 5905MHz from LAA are added.
    For 40 MHz BW: Select NREF with its corresponding RF reference frequency (FREF) is as close as to the WIFI 40MHz nominal center frequency. Two more center frequency on 5835MHz and 5875MHz is added.

## Slide 4: Proposal
    For 80 MHz BW: Select NREF with its corresponding RF reference frequency (FREF) is as close as to the WIFI 80MHz nominal center frequency. One more center frequency on 5855MHz is added.
    For 10 MHz BW: Select NREF with its corresponding RF reference frequency (FREF) is as close as to the center frequency of 5730 MHz and 5830 MHz, 10 MHz channel bandwidth shall only apply in certain regions where the absence of non 3GPP technologies can be guaranteed on a long term basis in this version of specification.
    For 60 MHz BW: FFS
    For 100 MHz BW: FFS
  CA is supported, FFS on other CA scenario to define new raster points. Companies are encouraged to bring Tdoc to suggest CA scenario at next meeting.
  Channel raster definition shall consider CA operation
    Allow PRB grid alignment between CC in contiguous CA
    Allow PRB grid alignment between wideband (>20MHz) and a LBT sub-band (20MHz) CC
    Down select channel raster & SSB raster entry such that it only support k_SSB = 0
    Support the same channel raster entry for 15 kHz, 30 kHz and 60 kHz for a given BW

## Slide 5: Information: channel Bonding in ETSI BRAN

## Slide 6: Ref
[1] R4-1907595, WF on band plan for NR-U 5GHz, Ericsson
[2] R4-1908875, "Channel raster in NR-U" (Qualcomm Incorporated).
[3] R4-1909003, "Channel raster for 5GHz NR-U band n46" (Nokia, Nokia Shanghai Bell).
[4] R4-1909008, "Channelization for NR-U in band n46" (Nokia, Nokia Shanghai Bell).
[5] R4-1908108, "Channel arrangement for NR-U" (Samsung).
[6] R4-1909392 “channel raster design of Rel-16 NR-U for 5GHz band” Ericsson
[7] R4-1909199, "Channel arrangement for NR-U band n46" (Huawei, HiSilicon).
[8] ETSI BRAN 301 893, v2.0.7

## Slide 7: background
The coexisting scenario is focus in NR-U WID objective [RP-191575]