## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 – 30 August, 2019
Ericsson
Way forward on Rel-16 MTC RRM enhancement
R4-1909491

## Slide 2: Wake-up signal
RAN4 shall wait for more RAN1 progress about WUS and shall discuss the possibility of reusing release 15 requirements at future meeting.

## Slide 3: MPDCCH performance improvement for RLM
MPDCCH BLER for improved RLM is evaluated using following MPDDCH parameters:
Parameters | Values
DCI format | 6-1A (CE Mode A)
System BW | 10MHz
Starting OFDM symbols | 2
(RL, AL) | Set 1: (4, 16) for Out-of-synch and (2, 4) for In-synch Set 2: (8, 24) for Out-of-synch and (4, 8) for In-synch
Transmission type | Distributed
Channel model | AWGN, EPA5, ETU30
Metric | In-synch: MPDCCH BLER of 2% Out-ot-synch: MPDCCH BLER of 10%
Frequency hopping | OFF
Reference signal | DMRS + CRS
Power offset between DMRS and CRS | 0dB
DMRS/CRS precoding | Cyclic precoder: Precoder granularity in frequency domain: [4]ms Precoder granularity in time domain: TBD Codebook: TBD

## Slide 4: Preconfigured UL resource
Number of RSRP thresholds for validating the TA using the serving cell RSRP change method is configured by the eNB and can have any of the values 1 or 2.
Relaxed serving cell monitoring shall not be allowed when the UE is configured to validate the TA using serving cell RSRP change method for PUR.
TA is validated using two measurements that are performed within following measurement window:
    The first measurement (RSRP1) shall be performed within following time range: T1 – N ≤ T1’ ≤ T1 + N;
    The second measurement (RSRP2) shall be performed within following time range: T2 – M ≤ T2’<T2;
    Where
        T1’ is the time when RSRP1 becomes available,
        T1 is the time when TA is obtained
        N is the number of DRX cycles and its value is TBD.
        T2’ is the time when RSRP2 becomes available,
        T2 is the time when TA is validated,
        M is the number of DRX cycles and its value is TBD.

## Slide 5: Mobility enhancement
The relaxation factor N for category M1/M2 UEs are defined as in Table 1 and 2 for normal DRX and eDRX respectively.
Table 1: The relaxation factor N for a category M1/M2 UE not configured with eDRX IDLE cycle
Table 2: The relaxation factor N for a category M1/M2 UE configured with eDRX IDLE cycle
RSS part is to be updated based on simulation results.
DRX cycle length [s] | Value
0.32 | Min(n , 16)
0.64 | Min(n , 8)
1.28 | Min(n , 4)
2.56 | Min(n, 2)
NOTE: n is signaled by the network by using TBD defined in TS 36.331 [2]. | 
DRX cycle length [s] | Value |  |  | 
 | 5.12 ≤ PTW length [s] < 7.68 | 7.68 ≤ PTW length [s] < 12.8 | 12.8 ≤ PTW length [s] < 23.04 | 23.04 ≤ PTW length [s]
0.32 | Min(n, 2) | Min(n , 4) | Min(n , 8) | Min(n , 16)
0.64 | N/A | Min(n, 2) | Min(n , 4) | Min(n , 8)
1.28 | N/A | N/A | Min(n, 2) | Min(n , 4)
2.56 | N/A | N/A | N/A | Min(n, 2)
NOTE: n is signaled by the network by using TBD defined in TS 36.331 [2]. |  |  |  | 

## Slide 6: DL quality reporting
RAN4 shall wait for further RAN1/RAN2 progress.