## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 – 30 August, 2019
Ericsson
Agreements for Rel-16 NB-IoT RRM enhancement
R4-1909495

## Slide 2: Group WUS
RAN4 shall wait for more RAN1 progress about WUS and shall discuss the possibility of reusing release 15 requirements at future meeting.

## Slide 3: Preconfigured UL resource
Number of RSRP thresholds for validating the TA using the serving cell RSRP change method is configured by the eNB and can have any of the values 1 or 2.
Relaxed serving cell monitoring shall not be allowed when the UE is configured to validate the TA using serving cell RSRP change method for PUR.
TA is validated using two measurements that are performed within following measurement window:
    The first measurement (RSRP1) shall be performed within following time range: T1 – N ≤ T1’ ≤ T1 + N;
    The second measurement (RSRP2) shall be performed within following time range: T2 – M ≤ T2’<T2;
    Where
        T1’ is the time when RSRP1 becomes available,
        T1 is the time when TA is obtained
        N is the number of DRX cycles and its value is TBD.
        T2’ is the time when RSRP2 becomes available,
        T2 is the time when TA is validated,
        M is the number of DRX cycles and its value is TBD.

## Slide 4: NRS presence on non-anchor carriers
RAN4 shall discuss NRSRQ measurement on non-anchor carrier and down-select among following options:
  Option #1: UE is allowed to use NRSRQ measurement performed on the non-anchor carrier provided that the magnitude of the difference between NRSRQ performed on the anchor and non-anchor is less than a certain margin (X dB).
  Option #2: NRSRQ is measured as follows when UE is camped on a non-anchor carrier:
  Option #3: UE is allowed to use the NRSRQ measurement on either anchor- or non-anchor carrier for serving cell evaluation by applying compensation.
  Option #4: UE shall evaluate the serving cell using NRSRP measurement only when camped on a non-anchor carrier.

## Slide 5: Msg3 based channel quality reporting
RAN4 assumes the measurement period for DL channel quality reporting in IDLE for non-anchor is between the beginning of MSG2 transmission to the beginning of MSG3 transmission.
For DL quality reporting in CONNECTED mode, RAN4 need to wait further the conclusion for measurement resources and message contents.