## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, Aug 26th - 30th, 2019
Huawei, HiSilicon
Way forward on UE sidelink timing requirements for NR V2X
R4-1909993

## Slide 2: Agreements on Te requirements for NR V2X (1)
NR V2X timing error requirement for GNSS as time reference:
  FFS the Te requirements for GNSS as time reference in FR2
NR V2X UE timing error requirement for NR SyncRef UE as time reference:
  FFS the Te requirements for NR SyncRef UE as time reference in FR2
Frequency Range | Te
FR1 | 12*64*Tc
FR2 | TBD
Frequency Range | SL SCS (kHz) | Te
FR1 | 15 | 12*64*Tc
 | 30 | 8*64*Tc
 | 60 | 5*64*Tc
FR2 | 60 | TBD
 | 120 | TBD

## Slide 3: Agreements on Te requirements for NR V2X (2)
UE timing error requirement for gNB as time reference for NR SL in FR1:
  FFS the feasibility on whether gNB in FR2 can be used as time reference for NR V2X UE in FR1.
FFS the UE timing error requirement for gNB as time reference for NR SL in FR2 if RF session defines FR2 band for NR V2X.
  FFS the feasibility on whether gNB in FR1 can be used as time reference for NR V2X UE in FR2.
Frequency Range of NR Uu | DL SSB SCS (kHz) | SL SCS in FR1 (kHz) | Te
FR1 | 15 | 15 | 14*64*Tc
 |  | 30 | 12*64*Tc
 |  | 60 | 12*64*Tc
 | 30 | 15 | 10*64*Tc
 |  | 30 | 10*64*Tc
 |  | 60 | 9*64*Tc
FR2 | 120 | 15 | TBD
 |  | 30 | TBD
 |  | 60 | TBD
 | 240 | 15 | TBD
 |  | 30 | TBD
 |  | 60 | TBD

## Slide 4: Agreements on Te requirements for NR V2X (3)
UE timing error requirement for eNB as time reference:
  FFS the feasibility on whether eNB can be used as time reference for NR V2X UE in FR2 if RF session defines FR2 band for NR V2X.
Frequency Range of NR SL | LTE DL CBW (MHz) | Te
FR1 | >=3 | 14*64*Tc
FR2 | >=3 | TBD

## Slide 5: For information
For the case where eNB or gNB are used as the reference source, Te= Error_DL+ Margin_SL + Interface error
  Error_DL = time chip granularity = Sampling time interval on DL
  Sampling time interval on DL = 1/ (∆fmax*Nf)
  where ∆fmax is SCS size and Nf is FFT size.
For the cases where synRefUE is usesd as the reference source, Te= Error_SL+ Margin_SL
  Error_SL = time chip granularity = Sampling time interval on SL
  Sampling time interval on SL = 1/ (∆fmax*Nf)
  where ∆fmax is SCS size and Nf is FFT size.
  Only specify the requirement when sidelink SSB SCS is aligned with the sidelink TX SCS.
Principle 1: non-increasing Te will be applied, if the SSB SCS size is fixed and SL SCS size is increased.
Principle 2: always use max Margin_UL value to derive the minimum requirement, if Margin_UL have different values for a single UL SCS associated with different DL SCS sizes.
Principle 3: the additional interface error between NR/LTE Uu and NR V2X should be considered
Based on the above principles, the values of Te for each case are calculated and the results show in attachment.