## Slide 1: Way Forward on LTE Mobility Enhancements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #92 R4-1910003
Ljubljana, Slovenia, 26-30 Aug 2019

## Slide 2: Conditional handover
Interpretation of “handover condition is met”
  Companies should analyse solution for decision in RAN4#92bis considering among other (see next page):
    CHO RRC configuration
    CHO condition fulfilled (before UE realizes)
    UE realizes CHO condition is fulfilled
    Etc.

## Slide 3: Conditional handover
Ending point of Conditional HO:
  Potential agreement:
    When PRACH is transmitted in target cell
Measurement
Report
CHO RRC
configuration
CHO condition
Fulfilled.
Execute CHO
PRACH

## Slide 4: Conditional handover
CHO delay requirement:
  The definition of when the CHO delay starts is FFS
  Exact delay equation is FFS
  UE RRC processing time is broken into two segments:
  First segment is immediately after RRC HO command reception
  Second segment is after UE realizes the condition is met and identity of target cell is determined
  Company input concerning each different delay for CHO

## Slide 5: Reduction of user data interruption
eMBB LTE handover delay definition:
  The legacy handover delay definition may not be suitable for simultaneous connectivity handover.
  The starting point of handover delay is defined as the time when UE receives RRC indicating handover. The ending point of handover delay is FFS.
  RAN4 needs to discuss if delay and interruption requirement is needed for source cell release.
  Company input concerning each delay and interruption requirement