## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 - 30 August, 2019
Huawei, HiSilicon
Way forward on NR Rel-15 BS demodulation requirements
R4-1910063

## Slide 2: General
Test Applicability rule
  Introduce new test applicability rule which states that if BS supports DFT-s-OFDM, BS should be tested without PT-RS
Declaration of support UL CA
  Add new declarations of the support of UL CA for PUSCH demodulation performance tests
Direction for BS type 1-O OTA test
  OTA REFSENS receiver target reference direction (D.54)
Uncertainty and TT
  Remove the square brackets for uncertainty and TT for FR1 and FR2 by bringing CRs for next meeting
Alignment of 38.141-1 and 38.141-2 test setup and procedure
  FFS alignment of 141-1 and 141-2 test setup and procedure steps split.

## Slide 3: OTA AWGN power level setting (1/2)
Add the following editor notes in the table for AWGN power level setting for OTA test:
  NOTE 1: ΔOTAREFSENS as declared in D.53 in Table 4.6-1 and section 7.1.
  NOTE 2: ΔFR2_REFSENS = -3dB as described in section 7.1, since the OTA REFSENS receiver target reference direction (as declared in D.54 in Table 4.6-1) is used for testing.
  NOTE 3: EISREFSENS_50M as declared in D.28 in Table 4.6-1.

## Slide 4: OTA AWGN power level setting (2/2)
Keep ΔFR2_REFSENS parameter in the AWGN power level derivation formula for BS type 2-O:
BS type | Sub-carrier spacing (kHz) | Channel bandwidth (MHz) | AWGN power level
BS type 2-O | 60 | 50 | EISREFSENS_50M + ΔFR2_REFSENS + 15 dBm / 47.52 MHz
 |  | 100 | EISREFSENS_50M + ΔFR2_REFSENS + 18 dBm / 95.04 MHz
 | 120 | 50 | EISREFSENS_50M + ΔFR2_REFSENS + 15 dBm / 46.08 MHz
 |  | 100 | EISREFSENS_50M + ΔFR2_REFSENS + 18 dBm / 95.04 MHz
 |  | 200 | EISREFSENS_50M + ΔFR2_REFSENS + 21 dBm / 190.08 MHz

## Slide 5: PUSCH
Performance for different duplex mode and TDD UL-DL patterns
  Apply the current PUSCH performance requirements to FDD mode
  Further discuss whether the requirements can be applied to other TDD configurations in the next meeting.

## Slide 6: PUCCH (1/3)
Test parameter configuration
  Change the test parameter of first PRB after frequency hopping configuration to “The largest PRB index - (number of PRBs - 1)”
Multi-slot PUCCH
  Only define multi-slot PUCCH requirements with 1T2R, See Slide#8 for the simulation assumptions
PUCCH format 2
  Add test parameter configuration for NID0 = 0

## Slide 7: PUCCH (2/3)
Notation in TS 38.104/141-1/141-2 for PUCCH |  | 
Current | Proposed update | Source
Modulation | Modulation order | TS 38.214 section 5.1.3
nrofBits or the number of UCI bits | The number of UCI information bits | TS 38.213 section 9.2
nrofPRBs | Number of PRBs | TS 38.213 section 9.2.1
startingPRB | First PRB prior to frequency hopping | TS 38.213 section 9.2.1
intraSlotFrequencyHopping | Intra-slot frequency hopping | TS 38.211 section 6.3.2.4.1
interSlotFrequencyHopping | Inter-slot frequency hopping | 
secondHopPRB | First PRB after frequency hopping | TS 38.213 section 9.2.1
pucch-GroupHopping | Group and sequence hopping | TS 38.331 section 6.3.2
hoppingId | Hopping ID | TS 38.331 section 6.3.2
initialCyclicShift | Initial cyclic shift | TS 38.213 section 9.2.1
startingSymbolIndex | First symbol | TS 38.213 Table 9.2.1-1
nrofSymbols | Number of symbols | TS 38.213 Table 9.2.1-1
Index of orthogonal sequence (time-domain-OCC) | Index of the orthogonal cover code (timeDomainOCC) | TS 38.211 section 6.3.2.4.1
occ-Length | Length of the orthogonal cover code | TS 38.213 section 9.2.1
occ-Index | Index of the orthogonal cover code | TS 38.213 section 9.2.1
Number of slots | Number of slots for PUCCH repetition | TS 38.213 section 9.2.6
PUCCH terminology:

## Slide 8: PUCCH (3/3)
Simulation assumptions for multi-slot PUCCH
Parameters |  | PUCCH Format 1
Bandwidth/SCS |  | 40 MHz/ 30kHz
Antenna |  | 1T2R
Propagation condition |  | TDLC300-100
Carrier frequency (GHz) |  | 4GHz
(#Bits, #Symbols, #PRBs) |  | (2, 14, 1)
Initial cyclic shift |  | 0
First symbol |  | 0
Index of orthogonal sequence (time-domain-OCC) |  | 0
Inter/Intra-slot frequency hopping |  | Inter-slot frequency hopping Enabled
 |  | Intra-slot frequency hopping disabled
Number of slot |  | 2
Test metric | DTX to Ack probability <1% | √
 | Missed Ack probability < 1% | √
 | NACK2ACK < 0.1% | √

## Slide 9: Simulation Results
Discuss how to handle the requirements still with TBD case by case in the next RAN4#92Bis meeting
Solve the those TBDs in the next RAN4#92Bis meeting