## Slide 1: WF for intra-band UL CA for FR1 power class 3
Agenda item: 9.12.4
Source: Huawei, HiSilicon, Qualcomm, Skyworks, [MediaTeK]
3GPP TSG-RAN WG4 #92 R4-1910273
Ljubljana, Slovenia, 26th – 30th August, 2019

## Slide 2: Agreement
RAN4 need to confine the number of component carrier to no more than two CCs for NR intra-band UL CA.

## Slide 3: Agreement
The following contents have been recorded in RAN4#92 Chairman notes
Proposal 1 assumptions for MPR studies:
• Power aspects: Single transmit path, equal PSD and equal back-off is used
• CCs: Same SCS and channel BW between 20 and 100 MHz
• Bands and channel configurations: % BW limitations (3% FDD, 4% TDD) should be considered for total transmitted BW and further back-off evaluated if exceeded (possibly with spectrum flatness relaxations)
Proposal 2 for contiguous NR UL CA MPR evaluation:
• SEM and ACLR requirements are based on the aggregated bandwidth with ACLR measurement bandwidths as follows:
• 100% aggregated bandwidth for wanted and 99% aggregated bandwidth for adjacent in FR1
• In band emissions and EVM are evaluated per subclause 6.5.2A [7].
Proposal 3 for non-contiguous NR UL CA MPR evaluation:
• SEM requirement uses the combined mask of each CC
• ACLR uses the individual CC definition for the outer adjacent channels with the wanted signal power equal to the total CC1 and CC2 power
• Due to issues with image rejection in the single transmitter case, it is suggested evaluate ACLR and define way forward (for example to ignore ALCR in the gap or to re-evaluate image rejection or ACLR requirement)
• In band emissions and EVM are evaluated per subclause 6.5.2A [7].

## Slide 4: Agreement
SEM table for intra-band contiguous CA can be introduced as below
ΔfOOB (MHz) | Spectrum emission limit (dBm) | Measurement bandwidth
± 0 - 1 | Max(Round(10*log(0.15/BWChannel_CA)),-24) | 30 kHz
± 1 - 5 | -10 | 1 MHz
± 5 - BWChannel_CA | -13 | 1 MHz
± BWChannel_CA– (BWChannel_CA+5) | -25 | 1 MHz
NOTE: BWChannel_CA refers to the aggregated channel bandwidth in MHz as defined in sub-clause 5.3A.3. |  | 
General spectrum emission mask for intra-band contiguous UL CA

## Slide 5: Reference
[1] R4-1908426 Inclusion of minimum and OFF power and occupied bandwidth for intra-band CA, vivo
[2] R4-1908839 Initial Measurement Results for Intra-band Contiguous NR UL CA for FR1, Skyworks Solutions Inc
[3] R4-1908968 [UL CA]discussion on Tx requirement for NR intra-band CA in 38.101-1, Huawei, HiSilicon
[4] R4-1908969 [UL CA]Draft CR for 38.101-1 adding Output RF spectrum emissions for CA, Huawei, HiSilicon
[5] R4-1909583 General Requirements for Intra-band Contiguous ULCA for FR1, Qualcomm Incorporated
[6] R4-1908840 Proposals on Intra-band NR UL CA Requirements for FR1, Skyworks Solutions Inc.
[7] TS 36.101 g20
[8] TS 38.101-3 g00