## Slide 1: WF on B41/n41 29 dBm Power Class and EN-DC A-MPR Improvement
Sprint, Qorvo

## Slide 2: Background
In [1] it was agreed to study potential improvements in intra-band EN-DC B41/n41 A-MPR resulting from revised assumptions, particularly higher antenna isolation.
  Goal is to agree on optional capability for improved R-IMD performance, which could be signaled by UEs capable of meeting new specification.
  UEs that cannot meet improved spec could not signal new capability, and comply with existing Rel-15 A-MPR curves.
While no agreement has been reached on large potential isolation improvements, new measurements [2,3,4] with 10 dB and 13 dB of isolation show room for improvement compared to Rel-15 A-MPR definition.
  Multiple reasons for differences, including improved measurement methodology compared to some data that informed Rel-15 definition.
  Improvements may be possible in important parts of the curves for real practical usage, including small allocations on -13 dBm/MHz curve, and large allocations on all curves
The 29 dBm HPUE work item includes the following objective:
  Assess the impact on Band 7, n7, 38 and n38 related to a 29 dBm UE power class

## Slide 3: -13 dBm/MHz A-MPR
10 dB Antenna Isolation
13 dB Antenna Isolation
Region of potential improvement

## Slide 4: -25 dBm/MHz A-MPR
10 dB Antenna Isolation
13 dB Antenna Isolation
Region of potential improvement

## Slide 5: -30 dBm/MHz MPR
10 dB Antenna Isolation
13 dB Antenna Isolation
Region of potential improvement

## Slide 6: Way Forward
Companies are encouraged to bring A-MPR measurement data for:
  Antenna isolations of 10 dB and 13 dB
  Post PA loss of 4 dB
  Power Class 2 Tx chains (LTE and NR)
  Equal Power on LTE and NR
  Various allocation combinations with range of aggregate BWs, with focus on “worst case” combinations (assumed to be near-equal allocation BWs).
  Determine backoff required to meet -13, -25, and -30 dBm/MHz SEM, and ACLR limits
  Goal is to take data from multiple sources and define new A-MPR curves accommodating different implementations. New A-MPR curve will be associated with Modified MPR bits and thus would be optional.
For impact of 29 dBm B41/n41 support to same UE support of B7/n7 and B38/38, companies agree that the impact is the same as for PC2 (26 dBm) B41 support, since the Tx chains may use the same hardware. Impact of PC2 impact to B7 and B38 was analyzed in [6].

## Slide 7: References
[1] R4-1907495, Way Forward on B41/n41 A-MPR assumptions, RAN4#92
[2] R4-1908252, A-MPR/MPR improvement for B41/n41 EN-DC, Intel
[3] R4-1908822, Discussion on Improved Isolation for 2PA Intra-band ENDC with Initial Measurement Results, Skyworks
[4] R4-1909939, Measurements for B14/n41 A-MPR with Varied Isolation, Sprint
[5] R4-1909902, 29 dBm In-Device Impact on Band 7/n7 and Band 38/n38, Sprint
[6] TR 36.886-e10, Band 41 High Power UE (HPUE)