## Slide 1: WF on FR2 Inter-band CA
Qualcomm Incorporated, Apple Inc.
R4-1910337
3GPP TSG-RAN WG4 Meeting #92
Ljubljana, Sl, 26-30 Aug 2019
Agenda: 9.13.7

## Slide 2: Background
A study is provided on the Network performance and testability may have challenges if UE is not capable for beamforming to same directions for both bands concurrently
If same hardware components are shared in the signal paths, large power imbalance will cause receiver SNR degradation since the other band will jam the other band. Similarly, shared HW can not process symbols with larger time difference than ½ CP

## Slide 3: WF
UE requirements will be applicable under moderate power imbalance, exact number is FFS
Companies are encouraged to study feasibility of existing 8 usec time difference requirement of the received symbols
For FR2 inter-band downlink CA (28 + 39 GHz), requirement derivation for spherical coverage assumption shall be studied in the next meeting. (e.g. whether UE is capable for forming beam towards the same directions and different directions which on both bands simultaneously)
  Impact of different directions only to multiband relaxations shall be part of study