## Slide 1: WF on spectrum utilization for NR-U
Nokia, Nokia Shanghai Bell
R4-1910388
3GPP TSG-RAN WG4 Meeting #92
Ljubljana, Slovenia, 26th - 30th August 2019

## Slide 2: Background
During RAN4#92 meeting the following contributions were discussed on NR-U spectrum utilization:
R4-1908847 On NR-U SU for single CC and wideband operation, Skyworks Solutions Inc.
R4-1908073 Spectrum utilization for NR-U, Samsung
R4-1909005 Increasing of spectrum utilization for NR-U, Nokia, Nokia Shanghai Bell
R4-1909200 Spectrum utilization improvement in unlicensed bands, Huawei, HiSilicon
This document summarizes the way forward on NR-U spectrum utilization

## Slide 3: Way forward (1/2)
Spectrum utilization for single carrier operation of 20MHz case:
It is agreed to increase the number of PRBs to 25 for 20 MHZ channel bandwidth with 60 kHz SCS with the awareness of relaxation on NR-U compared with R15 NR as below example for ACLR:
UE support of 60 kHz SCS is optional.
  UE supporting 20MHz CBW with 60kHz SCS andfor NR-U also supports 25 PRBs on the NR-U carrier;
  FFS: whether 25 PRBs for NR-U 20 MHz carrier is mandatory without capability or IOT bit is needed.
 | R15 NR FR1 | NR-U
BS ACLR | 45dB on 1st adjacent channel | 35dB on 1st adjacent channel
UE ACLR | 30dB on adjacent channel | TBD but majority view is less than (30dB or less)

## Slide 4: Way forward (2/2)
Spectrum utilization for wideband carrier(larger than 20MHz CHBW) operation:
Spectrum utilization will be revisit when intra-guard bands and number of intra-guards PRBs have been defined.
Spectrum utilization will be discussed based on emission related agreement.
This topic will be revisited after concluding requirements and assumption for UE capabilities to support 25 PRBs