## Slide 1: WF for NR-U BS RF requirements
Nokia, Nokia Shanghai Bell
R4-1910390
3GPP TSG-RAN WG4 Meeting #92
Ljubljana, Slovenia, 26th - 30th August 2019

## Slide 2: Background
During RAN4#92 meeting the following contributions were discussed on NR-U BS RF requirements:
R4-1909006 On BS RF requirements for NR-U, Nokia, Nokia Shanghai Bell
R4-1909204 NR-U BS ACLR requirements, Huawei, HiSilicon
Some earlier agreements on BS RF requirements for NR-U are capture in the WF from RAN#90 meeting:
R4-1902505, WF on NR-U BS RF requirements, Nokia, Nokia Shanghai Bell
This document summarizes the way forward on further NR-U BS RF requirements agreements.

## Slide 3: Way forward (1/2)
1. Following NR FR1 transmitter requirements can be reused for all CBWs for NR-U for single carrier case:
  BS output power,
  RE power control dynamic range,
  Transmitter transient period,
  Frequency error,
  Modulation quality,
  Time alignment error,
  Transmitter spurious emission,
  Transmitter intermodulation.
2. Total power dynamic range requirements shall not be applied for NR-U.

## Slide 4: Way forward (2/2)
3. To use following ACLR limits for all CBWs for NR-U:
  35 dB for first adjacent channel
  40 dB for second adjacent channel
4. Following NR FR1 receiver requirements can be reused for all CBWs for NR-U for single carrier case (new FRC(s) may need to be required) :
  In-band blocking,
  Out-of-band blocking,
  Receiver spurious emission,
  general Receiver intermodulation.
5. Following BS RF requirements require further studies for NR-U:
  UEM/OBUE
  Refsens
  In-channel selectivity
6. It is proposed to adopt the ETSI harmonized emission mask for UEM/OBUE.