## Slide 1: WF on UE RF requirements for NR V2X
Agenda item: 9.4.3
Source: LGE, Qualcomm, Vodafone, CATT, Huawei, [Futurewei]
3GPP TSG-RAN WG4 #92 R4-1910403
Ljubljana, Slovenia, 26th – 30th August, 2019

## Slide 2: Spec structure and clarification
Use suffix ‘E’ to specify NR V2X specific UE RF requirements for cases a new section needs to be added.

## Slide 3: Considerations on Operating band and channel arrangement
v
Sub- clause | Title | Considerations
5.2 | Operating bands | Operating band for only sidlelink V2X operation will be added based on operator’s request once licensed bands are approved in RAN4. Band n47 will be introduced
5.2E | Operating bands for V2X | Operating band for V2X operation will be added based on operator’s request once licensed bands are approved in RAN4. Band n47 will be added
5.3E | Channel bandwidth for V2X | Channel bandwidth for V2X will be decided based on industry demand and related regulation body’s decision. For n47, 10/20/40 CBW will be introduced and additional CBW are FFS.
5.4E | Channel arrangement for V2X | For ITS band operation, RAN4 need to discuss whether further optimization on channel/synchronization raster will be need.

## Slide 4: Considerations on Tx requirements
Sub- clause | Title | Considerations
6.2E | Transmitter power for V2X | For UE maximum output power, PC3 will be defined as baseline. Simulations for MPR and A-MPR will start after RAN1 agrees on parameters. For configured transmitted power, general principle for LTE V2X can be reused.
6.3E | Output power dynamics for V2X | For UE minimum output power, [-30dBm] can be reused as baseline. For Transmit OFF power, existing requirements of [-50dBm] could be reused. For ON/OFF time mask, existing ON/OFF time mask could be reused for standalone operation. [Switching time between LTE SL and NR SL in ITS spectrum can be studied for contiguous and non-contiguous cases separately.] Power control is FFS based on RAN1 progress.
6.4E | Transmit signal quality for V2X | For Frequency error and EVM, existing requirements of [LTE V2X] could be used as baseline. For IBE, existing LTE V2X requirement could be reused.
6.5E | Output RF spectrum emissions for V2X | For OBW, same principle will be applied for V2X specific CBW. For SEM, [LTE V2X] SEM mask for the same CBW could be reused. For ACLR, it will be defined based on the output of NR V2X coexistence study For Spurious emission, if frequency specific value is not specified, typical value of -30dBm could be reused For Transmit intermodulation, existing NR Uu requirement could be reused

## Slide 5: Considerations on Rx requirements
Sub- clause | Title | Considerations
7.3E | Reference sensitivity power level for V2X | To be defined for V2X specific band after RAN1 physical layer design is completed.
7.4E | Maximum input level for V2X | Existing LTE V2X requirement of [-22 dBm] may be reused.
7.5E | Adjacent channel selectivity for V2X | It will be defined based on the output of NR V2X coexistence study
7.6E | Blocking characteristics for V2X | For In-band/Out-of-band blocking, similar level of wanted signal(V2X) and interferer could be reused for given V2X CBW. For band n47, narrow band blocking isn’t needed.
7.7E | Spurious response for V2X | Similar level of wanted signal(V2X) and interferer could be reused for given V2X CBW.
7.8E | Intermodulation characteristics for V2X | Similar level of wanted signal(V2X) and interferer could be reused for given V2X CBW.

## Slide 6: Reference
R4-1908423 Discussion on system parameters for NR V2X band n47 vivo
R4-1908378 TP for band and bandwidth for NR V2X CATT
R4-1908809 Discussion on NR V2X UE RF requirements LG Electronics Finland
R4-1909918 On UE framework for NR-V2X in licensed bands Huawei, HiSilicon
R4-1908353 NR V2X UE Transmitter Characteristics Futurewei
R4-1908354 NR V2X UE RF Receiver Characteristics Futurewei
R4-1908970 [V2X] Discussion on MPR simulation assumption for NR V2X Huawei, HiSilicon
R4-1908377 Discussion on NR V2X UE RF requirements CATT
R4-1908396 Discussion on output RF spectrum emissions for NR V2X UE CATT
R4-1908422 Discussion on NR V2X UE RF requirements vivo
R4-1908379 TP for Tx requirements for NR V2X CATT
R4-1908380 TP for Rx requirements for NR V2X, CATT
R4-1909917 On switching time between LTE SL and NR SL, Huawei, HiSilicon