## Slide 1: A-MPR for n38 40 MHz co-existence
Huawei, [Nokia, Qualcomm]
3GPP TSG-RAN4 Meeting #92
Ljubljana, Slovenia, 26th– 30th August, 2019
R4-1910512

## Slide 2: Agreements
Based on input from [1] ~ [3] following A-MPR is agreed.
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS | LCRB*12*SCS | 
 |  | MHz | MHz | 
40 MHz | 2590 ≤ FC ≤ 2595 | ≥0, <2.88 | >0 | A1
 |  | ≥2.88, <14.4 | >max (0, 12*SCS*RBend - 3.6) | A2
 |  | ≥14.4, <23.4 | >10.8 | A3
 |  | ≥23.4, <32.4 | >16.2 | A4
 |  | ≥32.4 | >0 | A5
Modulation/Waveform |  | A1 | A2 | A3 | A4 | A5
 |  | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner
DFT-s-OFDM | PI/2 BPSK | [5] | [2] | [3] | [7] | [12]
 | QPSK | [5] | [2] | [3] | [7] | [12]
 | 16 QAM | [5] | [2] | [3] | [7] | [12]
 | 64 QAM | [5] |  | [3] | [7] | [12]
 | 256 QAM | [5] |  |  | [7] | [12]
CP-OFDM | QPSK | [5] | [4] | [5] | [8] | [12]
 | 16 QAM | [5] | [4] | [5] | [8] | [12]
 | 64 QAM | [5] | [4] | [5] | [8] | [12]
 | 256 QAM |  |  |  | [8] | [12]

## Slide 3: References
[1] R4-1905336 n38 40 MHz A-MPR, Nokia, Nokia Shanghai Bell,
[2] R4-1909181 A-MPR table for n38 40 MHz co-existence Huawei, HiSilicon
[3] R4-1909587 n38 A-MPR for Wide BW Qualcomm Incorporated