## Slide 1: WF on switching time and interruption for MIMO layer adaption
CATT
3GPP TSG-RAN WG4 Meeting #92 R4-1910590
Ljubljana, Slovenia, 26-30 Aug 2019

## Slide 2: Background
In the revised WID of power saving [1], it was agreed to study MIMO layer adaption between initial/default BWP and other BWPs.
  Specify the power saving techniques of UE adaptation to the maximum number of MIMO layers [RAN1, RAN2, RAN4]
    Specify configuration of a different MIMO layer configuration of the initial/default BWP compared with other BWPs of a Serving Cell. [RAN2, RAN4]
      Discuss whether to also extend this to define per-BWP MIMO layer configuration [RAN1, RAN2]
    Evaluate if switching and interruption times for UE dynamic adaptation to the maximum number of MIMO layers are needed and which case assuming a relationship between the number of RF ports and the MIMO layer configuration [RAN4]
  Note: Switching on/off the RF is part of the evaluation

## Slide 3: Background
In RAN4#92 meeting, several contributions [2-9] were received regarding the switching and interruption time for MIMO layer adaption.
From the companies’ contribution, the following 2 cases were analyzed.
    Case 1: Maximum number of MIMO layers is adapted as a part of the BWP change
    Case 2: Only the number of maximum MIMO layer is changed in the BWP before and after MIMO layer adaption

## Slide 4: Agreement
It is RAN4 common understanding that Per-BWP maximum MIMO layer configuration is beneficial
Dynamic adaption to the maximum number of MIMO layers shall comply with Rel-15 per-CC limit configured via RRC signalling.
The current BWP switch delay and interruption requirements for Type 1 and Type 2 UE in 38.133 are reused for MIMO layer adaption when the maximum number of MIMO layers is adapted as a part of the BWP change. (case 1)
Further study the switching delay and interruption requirements when only the number of maximum MIMO layer is changed in the BWPs before and after MIMO layer adaption. (case 2)
  e.g. the BWP center frequency, bandwidth and SCS… will keep unchanged during MIMO layer adaption.
  no further relaxation of the requirement compared to BWP switching delay and interruption for Type 1 and Type 2 UEs.
The above bullets are for downlink MIMO layer adaption. FFS for UL.
Notes: Qualcomm：Case 1, BWP requirement should be the starting point。
Intel: propose to remove tightening.
Nokia: disagree with QC comments. We should not consider further relaxation considering that current BWP requirements is already very relaxed.
MTK: propose both type 1 and type 2
CATT: the additional time for MIMO layer adaption can be done in parallel with those for applying new BWP parameter. No need to do further relaxation.
Huawei: For case 2, propose to add antenna port.
QC: What is the point of specifying case 2
CATT: to cover the case when only limited set of parameters are changed.

## Slide 5: Reference
[1] RP-190xxxx, revised WID: UE Power Saving in NR, CATT
[2] R4-1908364, Discussion on UE dynamic adaptation to the maximum number of MIMO layers, MediaTeck
[3] R4-1908382, Further discussion on MIMO layer adaptation, CATT
[4] R4-1908430, Further evaluation of switching and interruption time for UE antenna switching, vivo
[5] R4-1908439, Further evaluation of switching and interruption time for UE antenna switching, Qualcomm
[6] R4-1908669, UE switching and interruption times for dynamic adaptations in UE Power Saving schemes, Nokia
[7] R4-1909077, Discussion on general requirement for MIMO layer adaption, OPPO
[8] R4-1909078, Discussion on switching and interruption requirement for MIMO layer adaption, OPPO
[9] R4-1909098, Discussion on switching and interruption requirement for MIMO layer adaption, Huawei, HiSilicon