## Slide 1: WF on EN-DC HPUE FDD+TDD China Unicom, CHTTL, OPPO, China Telecom, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #92bis R4-1913077
Chongqing, China, 14th– 18th October, 2019

## Slide 2: Backgrounds (1/3)
The scope of PC2 FDD-TDD including the following two cases:
  Study starts from case 1, but case 2 is not precluded.
  Example band combination for this study is DC_3_n78
 | EN-DC maximum power | LTE maximum power | NR maximum power
Case 1 | 26dBm | 23dBm | 23dBm
Case 2 | 26dBm | 23dBm | 26dBm

## Slide 3: Backgrounds (2/3)
WF R4-1910338 was approved during RAN4#92
General
  The following options will be discussed for both case1 and case2.
Target on down selection on UE reporting capability solutions based on the following Options, and any new solution will not be discussed in RAN4#92bis.
  Option1 report EN-DC total Duty cycle(Duty threshold) based on DutyLTE*(PLTE/ P26) + DutyNR*(PNR/ P26) ≤ Duty threshold[2][6]
  Option2 report DutyLTE based on NR TDD sub-frame configuration[5]
  Option3 report DutyNR based on LTE fixed dutycycle with LTE maximum transmit power 23dBm[4]
  Option4 report SARratio based on DutyLTE*(PLTE/ P26) + SARratio*DutyNR*(PNR/ P26) ≤ 50%[5]
  Option5 report SARratio and EN-DC total Duty cycle(Duty threshold) based on DutyLTE*(PLTE/ P26) + SARratio*DutyNR*(PNR/ P26) ≤ Duty threshold[1]
  Option6 configure Plte lower than 23dBm based on LTE 100% dutycycle[3]
  Target on finishing this SI in RAN#86

## Slide 4: Backgrounds (3/3)
Summary of Proposal and Discussion in RAN4#92bis Ad-hoc in R4-1912911
Option 1
  Supportive: Qualcomm, Huawei, CHTTL
Option 2
  Supportive:
Option 3
  Supportive: [Samsung], vivo, [OPPO], Huawei, CMCC, China Unicom, CHTTL, Apple
  Samsung: need to restrict the sets of LTE config to up to two.
  Oppo: can support option 3 if there is only one LTE config from the UE capability update feasibility perspective.
  Huawei/CMCC: need to restrict the sets of LTE config to at least two.
Option 4
  Supportive:
Option 5
  Supportive: NTT Docomo, OPPO
Option 6
  Supportive: Ericsson
  Ericsson: We propose to include option 6 to be listed in the TR on top of option 1-5.

## Slide 5: Way Forward on NSA FDD+TDD HPUE
  Target on down selection one UE reporting capability solution among option1， option3 and option5 from Specification impacts、BS and UE implementation and Flexibility perspective.
    At least the option selected among 1, 3, 5 after further down selection shall be captured in a TP to the TR describing the method.
  In RAN4#93, whether to capture option 6 (different from option 1-5) in the TR can be further discussed due to some open issues.
  Any new solution will not be discussed in RAN4#93.
  Target on finishing this SI and TR37.815 in RAN4#93/RAN#86.

## Slide 6: reference
R4-1909060 Effective use of power of PC2 UE with two different UL bands NTT DOCOMO, INC.
R4-1908591 Further discussion on solutions for EN-DC FDD-TDD High Power UE CHTTL, China Unicom
R4-1908721 Increasing EN-DC power for FDD-TDD PC2 and PC3 Ericsson
R4-1908862 Discussion on different schemes for PC2 EN-DC (FDD+TDD) vivo
R4-1909080 About NSA FDD-TDD HPUE SAR OPPO
R4-1909908 Further consideration on SAR solutions for FDD+TDD HPUE Huawei, HiSilicon
R4-1910740 About NSA FDD-TDD HPUE SAR solutions OPPO
R4-1910812 further discussion on option3 for PC2 EN-DC (FDD+TDD) vivo
R4-1911264 Discussion on the UE capabilibity solutions for EN-DC FDD-TDD High Power UE CHTTL
R4-1911649 Discussion on NSA FDD-TDD HPUE SAR solutions China Unicom
R4-1911716 Discussion of HPUE ENDC FDD+TDD NTT DOCOMO, INC.
R4-1912484 Comparison of options for FDD-TDD PC2 duty cycle capability signaling Qualcomm Incorporated
R4-1912520 On SAR solutions for FDD+TDD HPUE Huawei, HiSilicon