## Slide 1: WF on EMC Test Configuration Reduction
Ericsson
3GPP TSG-RAN WG4 Meeting #94bis-e R4-2005475
Electronic Meeting, April 20th – April 30th 2020

## Slide 2: Background
In RAN#4-92, a discussion on the need for a test configuration reduction for EMC was proposed by Ericsson in R4-1908856.
The main focus of this discussion is the MSR BS.
The main argument for the proposed discussion has been the increase in the number of test configurations associated to various possible RAT combinations.
Ericsson has submitted different Tdocs to RAN#4 in order to provide elements to the discussion.
Companies following EMC discussion have expressed interest on understanding the scope of the proposal and the potential benefits of implementing EMC test configuration reduction.

## Slide 3: WF Agreement
Current testing of EMC requirements as specified in standards such as TS 37.113 [1] (MSR BS) or TS 37.114 [2] (AAS BS) is increasingly complex and considers many test configurations, due to various possible RAT combinations. However, the benefits of this reduction as well as the way to implement this reduction is still open. Alternatives to be considered for achieving a test configuration reduction can be:
  As presented in R4-2004562, EMC Testing for Conducted Immunity and Conducted Emissions is independent of the of the product (BS) characteristics and features, including the operating frequency or the Radio Access Technology (RAT).
  For radiated emissions the proposal to achieve a test configuration reduction can consider that EUT/BS typically have several different functions and numerous modes of operation associated with each function. The mode(s) that produce(s) the highest emissions could be selected for the final measurements.
  For Radiated Immunity testing the difference is in the test bed implementation outside of the chamber/shielding room used to monitor different RATs performance.
Companies interested on the EMC discussion shall provide elements analyzing the existance of redundancies in the Capability Sets (CS) used for EMC testing in MSR BS/AAS.
Companies interested on the EMC discussion shall provide input in the identification of the requirements to consider for both Immunity and Emmission testing.
Decision on how to implement the EMC test configuration reduction are FFS. Options can be:
  Direct modifications to the TS on conformance
  Open a WI targeting Release 17.
  Other options are not precluded.