## Slide 1: WF on LS Reply to ITU-R WP5D for the frequency ranges below 6 GHz
Agenda Item: 11.2
Document for: Approval
Source: Ericsson
3GPP TSG-RAN WG4 #94-e-Bis Tdoc R4-2005170
Electronic Meeting, 20 – 30 April, 2020

## Slide 2: Background
TSG RAN received the LS in [1] from ITU-R ,requesting parameters for IMT for sharing and compatibility studies
TSG RAN initiated a study item for IMT parameters when operating above 6 GHz
This Way-Forward concerns the LS reply for bands below 6 GHz:
  470-694 MHz, 694-960 MHz, 1710–1885 MHz, 1885-1980 MHz, 2010-2025 MHz, 2110-2170 MHz, 2500-2690 MHz, 3300-3400 MHz, 3600-3800 MHz, 4800-4990 MHz
The following input to RAN4 #94-e-Bis was received:
  Three discussion papers for the response [3] [4] [6]
  Two proposals for the LS response in [2] [5]

## Slide 3: Agreements (1)
The LS response should contain the following tables
  IMT technology related parameters (all bands), BS & UE
  AAS BS Beamforming antenna characteristics (1710 – 4990 MHz)
  NOTE 1: No beamforming assumed for UEs
  NOTE 2: No separate table for Deployment parameters. We only submit those parameters that RAN4 propose to change compared to ITU-R M.2292.
BS technology parameters are given with references to TS 38.104:
  Signal bandwidth: Spec reference, Signal bandwidth = NRB(SCS) x SCS x 12
  Rx Noise: 5 dB (WA), 10 dB (MR) & 13(LA) dB, Reference to BS class definitions
  SINR operating range: Based on TR 38.803 Annex F (ITU-R LS response)
UE technology parameters are given with references to TS 38.101-1:
  Signal bandwidth: Spec reference, Signal bandwidth = NRB(SCS) x SCS x 12
  Rx Noise: 9 dB
  SINR operating range: Based on TR 38.803 Annex F (ITU-R LS response)

## Slide 4: Agreements (2)
AAS BS antenna characteristics
  Scenarios included: Rural, Macro suburban, Macro urban, Small cell Outdoor/Micro urban
  Antenna pattern: Refer to ITU-R M.2101 (all scenarios)
  H/V front to back ratio (dB): [30] dB (all scenarios)
  Antenna polarization: Linear ±45°(all scenarios)
  Array ohmic loss: 2 dB
  BS maximum coverage angle in the horizontal plane: 120°(all scenarios)
NOTE: More details for the parameters are given in the E-mail discussion summary (R4-2005715), Issue #1.

## Slide 5: Open issues
IMT parameters not yet agreed:
  BS Average output power: TBD
  UE Average output power: TBD
AAS BS antenna characteristics not yet agreed:
  Scenarios included: [Small cell Indoor/Indoor Urban]
  Element gain: [8 dBi],[6 dBi],[related element spacing and beamwidth] [all scenarios]
  H/V beamwidth of single element (degrees): [80/65], [90/65], [90/90]
  Antenna array configuration: [8x8], [8x4], [16x8],[12x8],[12x8x2]
  H/V radiating element spacing: [0.6λ/0.9λ], [0.5λ/0.9λ], [0.5λ/0.5λ] , [0.5λ/0.7λ]
  Conducted power (before Ohmic loss) per antenna element: [25/28/31 dBm/100 MHz], [43 to 46 dBm],[only one value?]
  BS vertical coverage range: [90 - 100°, including mechanical/electrical/beamforming tilt]

## Slide 6: Proposed way-forward
The LS response from RAN4 to WP5D should be agreed at RAN4#95-e, to be sent directly to ITU-R WP5D
    NOTE: Next ITU-R WP5D is at the end of June, concurrent with TSG RAN. For this reason, the LS must be sent directly to WP5D from RAN4.
Further discussions between proponents are encouraged until the May meeting
  A Draft based on existing agreements to be further developed
  Focus on resolving remaining Open Issues

## Slide 7: References
RP-200042, “LS on parameters of terrestrial component of IMT for sharing and compatibility studies in preparation for WRC-23” (ITU-R WP5D).
R4-2003322, "Reply LS on IMT-2020 parameters for sharing and compatibility studies for frequency for WRC23" (CATT).
R4-2003323, "IMT parameters for the frequency ranges below 5 GHz" (CATT).
R4-2004541, "Reply of IMT parameters for other frequency ranges requested in RP-200042" (Huawei).
R4-2004729, "Draft LS to Parameters of terrestrial component of IMT for sharing and compatibility studies in preparation for WRC-23 (below 6 GHz)" (Ericsson).
R4-2004952, "Reply to ITU-R WP5D on IMT parameters for 470-4990 MHz" (Nokia, Nokia Shanghai Bell).