## Slide 1: WF on FR2 new FWA UE RF and RRM requirements
Huawei, HiSilicon, SoftBank…
R4-2005177
3GPP TSG-RAN WG4 #94bis-e
April 20th – 30th, 2020
Electronic meeting

## Slide 2: WF on Power budget format
It is encouraged to provide analysis on network performance of high order modulation, the assumption can referenced to TR 38.803 for coexistence study
Companies are encouraged to provide Link budget based on the format in table 1 and table 2 in the next RAN4 meeting
Parameter | Unit | Nominal value | Worst value
Operating bands | GHz | n257/n258 | 
Pout per element | dBm |  | 
# of antennas in an array |  | option 1: 8 Option 2: 16 | 
Total conducted power per polarization | dBm |  | 
Average antenna element gain | dBi |  | 
Antenna roll-off loss versus frequency | dB |  | 
Realized antenna array gain | dBi |  | 
Polarization gain | dB |  | 
Mismatch and transmission line loss including load pull | dB |  | 
Beam forming loss (phase shifter and amplitude error) | dB |  | 
Finite beam table | dB |  | 
Beam forming loss (one beam table fits all) | dB |  | 
Form factor integration losses | dB |  | 
Total implementation loss (nominal) | dB |  | 
Total implementation loss (worst case) | dB |  | 
Total implementation loss (best case) | dB |  | 
Peak EIRP (Nominal) | dBm |  | 
Max TRP(Worst value) , should ≤ 23dBm | dBm |  | 
Tolerance (+/-) | dB |  | 
Peak EIRP (Minimum) | dBm |  | 
Table 1: Power budget format for peak EIRP
Parameter | Unit | Value
Operating bands |  | n257/n258
Modulation |  | QPSK
SNR requirement | dB | -1.0
Bandwidth | MHz | 50
Thermal noise | dBm/Hz | 
Noise Figure | dB | 
Number of antenna in an array |  | option 1: 8 Option 2: 16
Array gain | dB | 
Element gain | dBi | 
Diversity gain | dB | 
Antenna gain roll-off over frequency | dB | 
Beamforming loss | dB | 
Total insertion loss | dB | 
REFSENS for 50MHz channel BW | dBm | 
Table 2: Link budget format for peak EIS

## Slide 3
WF on identification of RF requirement impacts
RF requirement impacts | Scope of the work in RAN4
Maximum TRP | 23dBm
Maximum EIRP | 43dBm
UE minimum peak EIRP | To be higher than PC3 (22.4dBm) due to greater beam gain
EIRP Spherical coverage | 85%-tile point and corresponding min EIRP is FFS
MPR/A-MPR | Re-evaluate the MPR/A-MPR based on the PC3 MPR framework.
Beam correspondence requirements | See Slide 4
REFSENS (EIS) | To be more sensitive than PC3 due to greater beam gain
EIS Spherical coverage | 85%-tile point and corresponding maximum EIS is FFS To be narrower coverage with lower EIS than PC3.
Minimum output power | Further discuss the exact value after power class requirement is finalized
RAN4 to study the RF requirement in below table due to introduction of new FR2 FWA UE
Spherical coverage percentage –tile is agreed as 85% for both transmitter and receiver

## Slide 4
WF on beam correspondence
Multi-band relaxation for new FWA UE
  specify MBR for the new FWA UE, reuse the framework agreed for Rel-16, the specific value is FFS
UE capability for beam correspondence is FFS
  Reuse the same capability framework for PC3 (bit-0 and bit-1)
  Side condition is FFS
  Companies are encouraged to provide the evaluation result on beam correspondence tolerance requirement:
    85% percentage of delta EIRP CDF is no more than [Y]dB
  The simulation assumption is as below:
UE RF parameter | unit | Value
Frequency band |  | n257/n258
Measurement grid | degree | 7.5o or 15o
# of element antennas |  | 8/16 elements with 1 panel
Polarization |  | Dual polarization
Phase error per antenna element(δpk) Amplitude error per antenna element(δak) | Degree/dB | δpk ~ N(0, σ2)with σ=[0~22o] δak ~ N(0, σ2)with σ=[0~2]dB
Error in RSRP estimation(Dk) | dB | Dk ~ N(0, 22)

## Slide 5: WF on CA RF requirement
general RF requirement | New FWA UE
Configured transmitted power CA | Reuse the definition for PC2/3/4
Transmit off power CA | Reuse the definition for PC2/3/4
On/off time mask CA | Reuse the definition for PC2/3/4
Power control CA | Reuse the definition for PC2/3/4
Transmit signal quality | Reuse the definition for PC2/3/4
Output RF spectrum emissions | Reuse the definition for PC2/3/4
Maximum input level | Reuse the definition for PC2/3/4
ACS | Reuse the definition for PC2/3/4
IBB | Reuse the definition for PC2/3/4
Spurious emissions | Reuse the definition for PC2/3/4
CA general requirement listed in Table 5 for new FWA UE can reuse the requirement specified for PC2/3/4.
For UL CA, the MPR requirement can reuse the framework defined for PC2/3/4, the specific value can be further evaluated.
CA Minimum output power is further discussed after power class requirement is finalized

## Slide 6: WF on initial RRM requirement identification
RAN4 to study the RRM impacts due to introduction of new FR2 FWA UE including but not limited to the following aspects:
FR2 measurement requirements in idle mode (PC1 can be taken as baseline)
Known condition for FR2 SCell activation requirements (PC1 can be taken as baseline)
FR2 intra- and inter-frequency measurement requirements (PC1 can be taken as baseline)
Perf part will start discussion in August RAN4 meeting.
Side condition for FR2 measurement
Applicable test directions for FR2 RRM tests
UE gain range for FR2 measurement

## Slide 7: Annex: Summary of power budget proposed in RAN4 #94bis-e
 |  | R4-2003535 |  | R4-2003345 |  | R4-2004865 |  | R4-2004778 | 
Parameter | Unit | Nominal value | Worst value | Nominal value | Worst value | Nominal value | Worst value | Nominal value | Worst value
Operating bands | GHz | n257/n258 |  |  |  |  |  |  | 
Pout per element | dBm |  | 12.0 |  | 12.5 |  |  | 11dBm | 
# of antennas in an array |  | 8 | 8 |  | 8 |  |  | 16 | 
Total conducted power per polarization | dBm |  | 21.0 |  | 21.5 |  |  | 23 | -1
Average antenna element gain | dBi |  | 3.3 |  | 4 |  |  | 4 | 0
Antenna roll-off loss versus frequency | dB |  | -1.5 |  | -2 |  |  | -1.5 | -0.2
Realized antenna array gain | dBi |  | 10.8 |  | 11 |  |  | 14.5 | 0
Polarization gain | dB |  | 2.5 |  | 2.8 |  |  | 2.8 | -0.5
Mismatch and transmission line loss including load pull | dB |  | -1.5 |  | -2.5 |  |  | -2 | -0.7
Beam forming loss (phase shifter and amplitude error) | dB |  | -1.4 |  | -0.5 |  |  | -0.5 | 0
Finite beam table | dB |  | 0 |  | -0.25 |  |  | -0.1 | 0
Beam forming loss (one beam table fits all) | dB |  | -0.5 |  | -3.5 -0.25 |  |  | -0.25 | 0
Form factor integration losses | dB |  | -5.0 |  | -3.5 |  |  | -2 | -1
Total implementation loss (nominal) | dB |  |  |  |  |  |  | -4.85 | 
Total implementation loss (worst case) | dB |  |  |  | -7 |  |  |  | -8.3
Peak EIRP (Nominal) | dBm |  |  |  |  |  |  | 35.48 | 
Tolerance (+/-) | dB |  |  |  |  |  |  |  | 3.5
Peak EIRP (Minimum) | dBm |  | 26.0 |  | 28.3 |  | 28.0 |  | 32

## Slide 8: Annex: Summary of Refsens budget proposed in RAN4 #94bis-e
 |  | R4-2003535 | R4-2004865 | R4-2004778
Parameter | Unit | Value |  | 
Operating bands |  | n257/n258 |  | 
Frequency range | GHz | 24.5 – 29.5 |  | 
Modulation |  | QPSK |  | QPSK
SNR requirement | dB | -1.0 |  | -1dB
Bandwidth | MHz | 50 |  | 50MHz
Thermal noise | dBm/Hz | -174.0 |  | -174
Noise Figure | dB | 10.5 |  | 11
Number of antenna in an array |  | 8 |  | 16
Array gain | dB | 9.0 |  | 12
Element gain | dBi | 3.3 |  | 4
Diversity gain | dB | 0.0 |  | 0
Antenna gain roll-off over frequency | dB | -1.5 |  | -1.5
Beamforming loss | dB | -1.5 |  | -0.25
Total insertion loss | dB | -6.0 |  | -8.3
REFSENS for 50MHz channel BW | dBm | -90.8 | -92 | -93.3