## Slide 1: WF on supporting 30k SSB SCS for n34, n38, n39 and n50
Ericsson
R4-2005196
3GPP TSG-RAN WG4 Meeting #94-e-bis
Electronic meeting, 20 – 30 April 2020

## Slide 2: Background
Adding 30k SSB for n34, n39 and n50
  does not require support of multiple numerology for SSB and RX data while keeping the 15k SSB option for larger cells
  but imposes a penalty on cell-search time and a proposal contrary to earlier agreements
Adding 30k SSB for n38
  allows compatibility with the overlapping n41 (supports both 15k and 30k) using the same SSB pattern for 30k
  does not require support of multiple numerology for SSB and RX data while keeping the 15k SSB option for larger cells
  but imposes a penalty on cell-search time and a proposal contrary to earlier agreements

## Slide 3: Company views: no consensus
Several companies support adding 30k for n34, n38 ,n39 and n50
but concerns raised with cell-search time and revisiting earlier agreements on SSB SCS
for n38 concern with adding 30k since 15k is available for roaming with n41
for n39 the situation is unclear in Japan

## Slide 4: (one possible) Way forward
Given the lack of consensus
Consider a change from 15k to 30k SSB for n34 and n39 and n50
Consider addition of 30k SSB for n38 to allow use of the overlapping n41 (supporting both 15k and 30k SSB) ecosystem without restrictions
with due account of NBC issues