## Slide 1: WF on CA channel spacing for channel bandwidth pairs where no common u is found
Huawei, HiSilicon, [ ]…
R4-2005198
3GPP TSG-RAN WG4 #94bis-e
April 20th – 30th, 2020
Electronic meeting

## Slide 2: Background
Currently, Nominal channel space for CA is specified with, where the reference table for μ0 is Table 5.3.5-1:
While in Table 5.3.5-1, there is some cases that no common largest μ can be found:
 | NR band / SCS / E Channel bandwidth |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 904 MHz | 100 MHz
n40 | 15 | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |  |  | 
 | 30 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  | 
 | 60 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  | 
n41 | 15 |  | Yes | Yes | Yes |  |  | Yes | Yes |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes | Yes
 | 60 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes | Yes
n50 | 15 | Yes | Yes | Yes | Yes |  |  | Yes | Yes |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes3 |  | 
 | 60 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes3 |  | 
Table 5.3.5-1 Channel bandwidths for each NR band

## Slide 3
WF: No common μ can be found for some intra-band CA case
RAN4 need to consider the case for No common largest μ can be found for intra-band CA, and find a way to specify the nominal channel space for such case
How to deal with the issue will further discuss in next meeting:
  Option1:change the reference Table for µ0 adoption from Table 5.3.5-1 to Table 5.3.2-1 to ensure the common largest µ can be found.
  Option2: a specific provision to cover the corner cases
  Other options are not precluded
SCS (kHz) | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | 79 | 106 | 133 | 160 | 216 | 270 | N/A | N/A | N/A | N/A
30 | 11 | 24 | 38 | 51 | 65 | 78 | 106 | 133 | 162 | 217 | 245 | 273
60 | N/A | 11 | 18 | 24 | 31 | 38 | 51 | 65 | 79 | 107 | 121 | 135
Table 5.3.2-1: Maximum transmission bandwidth configuration NRB

## Slide 4
Reference
[1] R4-2004776 “on channel space for CA”, Huawei, HiSilicon, RAN4#94bis-e
[2] R4-2005087 ”email discussion summary on system parameter Rel-15”, ZTE, RAN4#94bis-e