## Slide 1: WF on aligning ACLR MBW definition between FR1 and FR2
Anritsu, Skyworks
R4-2005213
3GPP TSG-RAN WG4 Meeting #94-e-bis
Online, 20th Apr – 30th Apr 2020
Agenda: 4.4
E-mail title: [94e Bis][2] NR_NewRAT_UE_RF_Part_1
Sub-topic: 10-1
WI: NR_newRAT-Core

## Slide 2: Background on FR2 ACLR MBW issue
At RAN4 #94-e, the following issues related to position of ACLR MBW were discussed [1]:
- Current specification uses a MBW equal to Transmission Bandwidth Configuration but centered on the wanted and adjacent channels
- This does not account for the half SCS Shift and thus results in the transmission signal not being fully captured in the ACLR measurement BW for all cases.

## Slide 3: Background on FR2 ACLR MBW issue
Two solutions were proposed during #94-e and a concern of an impact to the regulatory requirements was raised with option 1:
Option 1: modify FR2 MBW according to FR1 method where MBW is increased by 1 SCS and stays centered on the channels
Option 2: maintain existing FR2 MBW, and change the text defining the center frequency of the measurement BW for the wanted channel so that MBW becomes centered on the Transmission Bandwidth Configuration.

## Slide 4: Background on FR2 ACLR MBW issue
WF at #94-e is cited as follows. [2]
In order to minimize the impact on the specification the following is proposed:
If no impact on existing regulatory is confirmed, use option 2 from R4-2002144:
  Keep ACLR measurement bandwidth as is
  Change the ACLR measurement bandwidth from centered on the channel to centered on the Transmission Bandwidth Configuration for the wanted signal and measurement bandwidth offset for adjacent channels stay at +/- channel BW
Bring CR in April meeting to change the text in 38.101-2 Table 6.5.2.3-1 accordingly
For both release 15 and release 16

## Slide 5: Analysis of 3GPP specs and Japanese regulation
At #94-e-bis, analysis of influence to the Japanese regulation was provided for both option 1 and option 2 [3], and observations are as follows.
Observation 1: Current definitions of measurement bandwidth for ACLR are aligned between 3GPP spec and Japanese regulation.
Observation 2: For option 1, modification of definition with duration of measurement bandwidth is necessary also in Japanese regulation.
Observation 3: For option 1, if the correction of the measurement bandwidth definition is allowed in Japanese regulation, all the conditions will be aligned between frequency ranges and also between 3GPP spec and Japanese regulation.
Observation 4: For option 2, modification of definition in center frequency of measurement bandwidth is necessary also in Japanese regulation.
Observation 5: For option2, misalignment of MBW conditions between frequency ranges will still be kept within both 3GPP spec and Japanese regulation.
Observation 6: Both option 1 and option 2 require changes in the definition of measurement bandwidth in Japanese regulation.

## Slide 6: Way forward (1)
Considering the consistency between FR1 and FR2, and also to align definitions of MBW between 3GPP and Japanese regulation, following proposals are made:
1) Override the previous decision in R4-2002827 [2] and apply the following change to ACLR MBW definition in FR2.
Modify FR2 MBW according to FR1 method where:
- the assigned NR channel power remains centered on the assigned channel frequency,
- the adjacent NR channel power remains centered on the NR channel frequency at nominal channel spacing,
and the MBW is increased by 1 SCS of the SCS that corresponds to the lowest guard-band of the channel bandwidth.
2) Bring CR at #95-e in May for both Rel-15 and Rel-16.
Associated MBW settings are shown on the next slide.

## Slide 7: Way forward (2)
Proposed ACLR MBW for FR2 (TS 38.101-2, Table 6.5.2.3-1)
 | Channel bandwidth / NRACLR / Measurement bandwidth |  |  | 
 | 50 | 100 | 200 | 400
 | MHz | MHz | MHz | MHz
NRACLR for band n257, n258, n261 | 17 dB | 17 dB | 17 dB | 17 dB
NRACLR for band n260 | 16 dB | 16 dB | 16 dB | 16 dB
NR channel measurement bandwidth [MHz] | 47.52 47.58 | 95.04 95.16 | 190.08 190.20 | 380.16 380.28
Adjacent channel centre frequency offset (MHz) | +50 | +100 | +200 | +400
 | / | / | / | /
 | -50 | -100 | -200 | -400

## Slide 8: Reference
[1] R4-2002144, “FR2 ACLR Measurement Bandwidth Definition”, Skyworks Solutions, inc., RAN4 #94-e, Online
[2] R4-2002827, “WF on FR2 ACLR MBW”, Skyworks Solutions Inc., RAN4 #94-e, Online
[3] R4-2003329, “Comparison of ACLR MBW definition with regulation in Japan”, Anritsu Corp., RAN4 #94-e-bis, Online

## Slide 9: Appendix A: Relation of ACLR MBW (CBW 100MHz, SCS 120kHz)

## Slide 10: Appendix A: Relation of ACLR MBW (CBW 100MHz, SCS 120kHz)
Option | Meas. BW | Center of Meas. BW | Remarks
Current | fullRB * 12 * SCS (same as Tx BW) | Fc | Meas. BW lacks half subcarrier width at the left side spectrum
1 | (fullRB * 12 + 1) * SCS | Fc | Meas. BW is wider than Tx BW by one subcarrier width
2 | fullRB * 12 * SCS (same as Tx BW) | Fc – SCS/2 | Center of Meas. BW is shifted to the left by half subcarrier

## Slide 11: Appendix B: Comparison b/w 3GPP and Japanese regulation
Comparison of 3GPP and Japanese regulation for ACLR with modification option 1 [3]
FR1 | 3GPP spec | Center frequency of Measurement BW = Center frequency of Channel BW Measurement BW = Maximum transmission bandwidth configuration + 1 SCS | Measurement condition is technically correct.
 | Japanese regulation | Same as 3GPP. | 
FR2 | 3GPP spec | Center frequency of Measurement BW = Center frequency of Channel BW Measurement BW = Maximum transmission bandwidth configuration + 1 SCS | Measurement condition becomes correct.
 | Japanese regulation | Aligned with 3GPP if the correction of MBW duration is allowed. | Measurement condition becomes correct if the change is allowed.
Alignment of definitions between FR1 and FR2: 3GPP: Aligned Japanese regulation: Aligned if the definition of measurement bandwidth can be corrected. |  |  | 
Alignment of definitions between 3GPP and Japanese regulation: Aligned on condition that the correction of measurement bandwidth definition is allowed in Japanese regulation. (Most recommended situation in which all the conditions are aligned between frequency ranges and also between 3GPP and Japanese regulation.) |  |  | 
Considerable impact to Japanese regulation: FR1: No impacts. FR2: Duration of measurement bandwidth is increased with one more SCS. ⇒ The modification is rather the change of measurement condition and no impact to the requirement. |  |  | 

## Slide 12: Appendix B: Comparison b/w 3GPP and Japanese regulation
Comparison of 3GPP and Japanese regulation for ACLR with modification option 2 [3]
FR1 | 3GPP spec | Center frequency of Measurement BW = Center frequency of Channel BW Measurement BW = Maximum transmission bandwidth configuration + 1 SCS | Measurement condition is technically correct.
 | Japanese regulation | Same as 3GPP. | 
FR2 | 3GPP spec | Center frequency of Measurement BW = Center frequency of Channel BW -1/2 SCS Measurement BW = Maximum transmission bandwidth configuration | Measurement condition becomes correct.
 | Japanese regulation | Aligned with 3GPP if the modification of center frequency of MBW is allowed. | Measurement condition becomes correct if the change is allowed.
Alignment of definitions between FR1 and FR2: 3GPP: Not aligned with both center frequency of MBW and duration of MBW. Japanese regulation: Not aligned with both center frequency of MBW and duration of MBW. |  |  | 
Alignment of definitions between 3GPP and Japanese regulation: Aligned only between same frequency ranges on condition that the correction of center frequency of measurement bandwidth definition is allowed in Japanese regulation. (Not a straightforward way for the correction.) |  |  | 
Considerable impact to Japanese regulation: FR1: No impacts. FR2: Center frequency of measurement bandwidth needs to be shifted 1/2 SCS, which is different definition with FR1. |  |  |