## Slide 1: WF on NR-U UE Rx requirements
Qualcomm Incorporated
R4-2005222
3GPP TSG-RAN WG4 #94-e-Bis
April 20th ‒ 30th, 2020
Electronic Meeting

## Slide 2: Background
NR-U WID in RP-192926 and all objectives therein apply
For LAA and eLAA, it is recognized that receiver characteristics are specified with 20 MHz interferer bandwidth for both non-CA and CA.

## Slide 3: Reference sensitivity
  REFSENS for Band n46
  The reference sensitivity minimum requirements should be the same regardless if intraCellGuardBandDL-r16, if supported, are configured or scheduled.
  REFSENS for 10MHz channel BW shall be defined for CA purpose, but not for other Rx requirements.
  REFSENS RMC is specified with all sub-bands and all RB’s within the DL channel allocated with intra-cell guard bands configured to zero.
  UL configuration is all sub-bands and all RB’s fully allocated using DFT-S-OFDM

## Slide 4: ACS
In-channel ACS requirement is not specified
Bandwidth of interfering signal is [fixed 20 MHz] for all cases including single carrier [and CA]
Single carrier
  For ACS Case 1
    Wanted signal power is REFSENS + 14 dB
    ACS for 20 MHz CBW is FFS dB; i.e., power of interferer is REFSENS+32.5 dB
  Case 2
    Not specified
Intra-band contiguous CA
  FFS

## Slide 5: In-band blocking
In-channel blocking requirement is not specified
Bandwidth of interfering signal is [fixed 20 MHz] for all cases including single carrier [and CA]
Single carrier wanted signal parameters
Intra-band contiguous CA
  FFS

## Slide 6: Out-of-band blocking
Range 3 power level to -20 dBm (to enable common filtering between 5 GHz and 6 GHz bands)
  NOTE 5: The power level of the interferer (PInterferer) for Range 3 shall be modified to -20 dBm, for FInterferer > 4200 MHz.
Wanted signal power at REFSENS + 9 for all CBW [including intra-band CA]
Out-of-band blocking details for EN-DC is FFS

## Slide 7: Narrowband blocking
Not specified for NR-U
  Narrowband signals are not expected in 5 GHz and 6 GHz bands