## Slide 1: WF on MPR/A-MPR requirements for S-SSB transmission
Qualcomm
3GPP TSG-RAN WG4 NR #94-e-Bis
20th - 30th Apr 2020
R4-2005225

## Slide 2: S-SSB MPR_A-MPR candidate options
Issue 1-3-1: MPR for S-SSB transmission
  Option 1: The allowed MPR of NR V2X S-SSB follow the NR Uplink MPR requirements specified in sub-clause 6.2.2 from TS 38.101-1. The MPR value is same for each of the channels for S-SSB transmission.
  Option 2: Define the new MPR requirements for NR V2X S-SSB based on simulation results. The MPR value is same for each of the channels for S-SSB transmission. MPR requirements based on inner, outer allocations1.
  Option 3: Define the new MPR requirements for NR V2X S-SSB based on simulation results. The MPR value is different for each of the channels for S-SSB transmission. MPR requirements based on inner, outer allocations1.
Issue 1-3-2: A-MPR for S-SSB transmission
  Option 1: Define A-MPR requirements for both 10MHz (EU NS_33) and 40MHz (FCC NS_48) according to inner/outer regions. Consider the merged A-MPR values (using average manner) from interested companies. The A-MPR value is same for each of the channels for S-SSB transmission.
  Option 2: Define A-MPR requirements for both 10MHz (EU NS_33) and 40MHz (FCC NS_48) according to inner/outer regions. Consider the worst A-MPR values from interested companies. The A-MPR value is same for each of the channels for S-SSB transmission.
  Option 3: Define A-MPR requirements for 10MHz (EU NS_33) and 10MHz (EU NS_NEW) without coexistence and 40MHz (FCC NS_48) according to RB start. Consider the worst A-MPR values from interested companies. The A-MPR value is same for each of the channels for S-SSB transmission.
  Note1: Inner and outer allocations based on sect. 6.2.2 TS38.101-1

## Slide 3: WF on MPR/A-MPR requirements for S-SSB transmission
The following options are suggested as a WF on MPR/A-MPR requirements for S-SSB transmission:
Issue 1-3-1: MPR for S-SSB transmission
  Option 2: Define the new MPR requirements for NR V2X S-SSB based on simulation results. The MPR value is same for each of the channels for S-SSB transmission. MPR requirements based on inner, outer allocations1.
 |  |  | MPR (dB) | 
Carrier Frequency (MHz) | Channel BW (MHz) | SCS (kHz) | Outer RB Allocations | Inner RB Allocations
XXXX | 10 | [ ] | ≤ [ ] | ≤ [ ]
 |  | [ ] | ≤ [ ] | ≤ [ ]
YYYY | 20 | [ ] | ≤ [ ] | ≤ [ ]
 | 30 | [ ] |  | ≤ [ ]
 |  | [ ] |  | ≤ [ ]
 | 40 | [ ] | ≤ [ ] | ≤ [ ]
 |  | [ ] |  | ≤ [ ]
Table 1- Sample MPR requirements
  Note1: Inner and outer allocations based on sect. 6.2.2 TS38.101-1

## Slide 4: WF on MPR/A-MPR requirements for S-SSB transmission
Issue 1-3-2: A-MPR for S-SSB transmission
  Option 3: Define A-MPR requirements for 10MHz (EU NS_33) and 10MHz (EU NS_NEW) without coexistence and 40MHz (FCC NS_48) according to RB start. Consider the worst A-MPR values from interested companies.
Carrier Frequency (MHz) | RBStart | A-MPRBase (dB) | AMPRStep (dB)
XXXX | ≤[ ] | ≤ [ ] | ≤ [ ]
 | >[ ] and ≤[ ] | ≤ [ ] | 
 | >[ ] and ≤[ ] | ≤ [ ] | 
 | >[ ] and ≤[ ] | ≤ [ ] | 
 | >[ ] and ≤[ ] | ≤ [ ] | 
 | >[ ] and ≤[ ] | ≤ [ ] | 
 | >[ ] and ≤[ ] | ≤ [ ] | 
YYYY | ≤[ ] | ≤ [ ] | ≤ [ ]
Table 2- Sample A-MPR requirements