## Slide 1: WF on NR Mobility Enhancements RRM requirements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #94-e-bis R4-2005305
Electronic Meeting, April 20th – April 30th 2020

## Slide 2: Background
Agreements in this way forward are based on email discussion in R4-2005392 Email discussion summary for [94e Bis][108] NR_Mob_enh_RRM
Agreements in the last RAN4#94-e meeting can be found in:
  R4-2002173 Email discussion summary for RAN4#94e_#50_NR_Mob_enh_RRM
  R4-2002224 WF on NR Mobility Enhancements RRM requirements

## Slide 3: DAPS handover: Agreement in 1st round
Issue 1-1: Interruption in intra-frequency DAPS HO D1 for 60KHz
Agreement: 4 slots
Issue 1-2: interruption when UL Tx overlap in time
Agreement: no need to capture this in RAN4 specification since corresponding UE behaviour has already been captured in RAN1 specification.
Issue 1-3: different interruption during Delay (1) and (2)
Agreement: different interruption during Delay (1) and (2) has already been considered and reflected in existing specification. RAN4 will not revisit previous agreement
Issue 1-4: Power imbalance in side condition for interruption requirements
Agreement: RAN4 will not capture side condition of power imbalance in core requirement. The issue can be discussed in performance part.
Issue 1-8: RRM measurement during DAPS handover:
Agreement: it is up to UE implementation whether to perform RRM measurement on the frequencies of source cell and target cell during DAPS handover procedure.

## Slide 4: DAPS handover: way forward for 2nd round
Side condition for sync DAPS HO regarding MRTD/MTTD at UE side is to be introduced. If side condition is not met, async DAPS HO is assumed.
The followings will be decided in RAN4#-95-e
  Whether the existing interruption requirements for intra-frequency DAPS HO are only applied for sync scenario.
  Whether the existing interruption requirements for intra-band inter-frequency DAPS HO are only applied for sync scenario.

## Slide 5: DAPS handover: way forward for 2nd round – cont.
Side condition for intra-frequency sync DAPS HO:
  UE which only support sync DAPS HO shall meet existing DAPS HO requirement as long as:
    Option 1: it is assumed that source and target cells are co-located.
      3 us MRTD and 5.21 us MTTD between source and target cells is not exceeded: Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
    Option 2: it is assumed that source and target cells can be non-co-located.
      33 us MRTD and 34.6 us MTTD between source and target cells is not exceeded Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
    Option 3: specify “Tight Sync” and “Loose Sync” for sync DAPS handover capabilities.
      Tight Sync : 3 us MRTD and 5.21 us MTTD between source and target cells is not exceeded: Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
      Loose Sync : 33 us MRTD and 34.6 us MTTD between source and target cells is not exceeded Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
Side condition for intra-band inter-frequency sync DAPS HO:
  UE which only support sync DAPS HO shall meet existing DAPS HO requirement as long as:
    Option 1: it is assumed that source and target cells are co-located.
      3 us MRTD and 5.21 us MTTD between source and target cells is not exceeded: Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
    Option 2: it is assumed that source and target cells can be non-co-located.
      33 us MRTD and 34.6 us MTTD between source and target cells is not exceeded Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
    Option 3: specify “Tight Sync” and “Loose Sync” for sync DAPS handover capabilities.
      Tight Sync : 3 us MRTD and 5.21 us MTTD between source and target cells is not exceeded: Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
      Loose Sync : 33 us MRTD and 34.6 us MTTD between source and target cells is not exceeded Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.

## Slide 6: DAPS handover: way forward for 2nd round – cont.
Side condition for FR1-FR1 inter-band sync DAPS HO:
  UE which only support sync DAPS HO shall meet existing DAPS HO requirement as long as:
    maximum of 33 us MRTD and 34.6 us MTTD between source and target cells is not exceeded.
Side condition for FR1-FR2 inter-band sync DAPS HO:
  UE which only support sync DAPS HO shall meet existing DAPS HO requirement as long as:
    maximum of 25 us MRTD and 26.1 us MTTD between source and target cells is not exceeded.

## Slide 7: DAPS handover: way forward for 2nd round – cont.
Other conditions for intra-frequency DAPS HO:
Intra-frequency DAPS HO requirements apply only if
  the centre frequency of the SSB of the source cell and the centre frequency of the SSB of the target cell are the same, and
  the subcarrier spacing of the two SSBs are also the same
  the active BWP of source cell contains the initial BWP of source cell.
  the active BWP of target cell contains the initial BWP of target cell.
  active DL/UP BWPs of target cell is confined within the active DL/UL BWPs of source cell