## Slide 1: WF on NR V2X RRM requirements
LG Electronics, MediaTek
3GPP TSG-RAN WG4 #94e-bis
Electronic Meeting, Apr.20th – Apr.30th 2020
R4-2005310

## Slide 2
NR V2X RRM part 1

## Slide 3
Issue 2-1: Rx Dropping Rate for selection/reselection of NR V2X synchronization reference source
  Keep the current Rx dropping rate requirement
Issue 2-2: Simulation assumptions for PSBCH-RSRP measurements evaluation
  Add TDL-C with 30ns, 1400Hz in propagation condition
Define interruption requirement of 1ms for sync source change as followings
  Issue 3-1-2: Interruption for sync source change between GNSS and a syncRef UE that is synchronized to gNB/eNB directly or in-directly
  Issue 3-1-3: Interruption for sync source change between GNSS and a syncRef UE that has the lowest priority
  Issue 3-1-4: Interruption for sync source change between GNSS and gNB/eNB
  Issue 3-1-5: Interruption for sync source change between gNB/eNB and a syncRef UE that is synchronized to GNSS directly or in-directly
  Issue 3-1-6: Interruption for sync source change between gNB/eNB and a syncRef UE that is synchronized to gNB/eNB directly or in-directly
  Issue 3-1-7: Interruption for sync source change between gNB/eNB and a syncRef UE that has the lowest priority
  Issue 3-1-9: Interruption for sync source change between a syncRef UE that is synchronized to GNSS directly or in-directly and another syncRef UE that is synchronized to gNB/eNB directly or in-directly
  Issue 3-1-10: Interruption for sync source change between a syncRef UE that is synchronized to GNSS directly or in-directly and another syncRef UE that has the lowest priority
  Issue 3-1-12: Interruption for sync source change between a syncRef UE that is synchronized to gNB/eNB directly or in-directly and another SyncRef UE that has the lowest priority
Issue 3-3: Whether to define RRM requirement related to concurrent operation with Uu and SL
  Do not define RRM requirement related to concurrent operation with Uu and SL
Issue 4-1: Whether to define SL RLM requirement
  Do not define SL RLM requirements
Issue 5-1-1: Terminology V2X vs SideLink in Rel-16
  Use ‘V2X’ terminology for RAN4 specification
Information on 1st round agreements

## Slide 4
Issue 2-2 : Simulation assumptions for PSBCH-RSRP measurements evaluation
  Clarify how many PSBCH symbols are used
  Encourage companies to provide simulation results in RAN4#95-e meeting based on R4-2005311
Issue 3-1-x : Interruption due to source change between GNSS and gNB/eNB, or GNSS and SyncRefUE, or gNB/eNB and SyncRefUE, or SyncRefUE and SyncRefUE
  Interruption requirement 1ms applies
    when the two synchronization sources that UE switches between are not synchronized or
    when the two synchronization sources that UE switches between are synchronized and they are from different type of sources listed below,
      GNSS and gNB/eNB or
      GNSS and SyncRefUE or
      gNB/eNB and SyncRefUE
WF

## Slide 5
Issue 3-1-1: Interruption for sync source change between GNSS and a syncRef UE that is synchronized to GNSS directly or in-directly
  Follow Issue 3-1-x’s agreement
Issue 3-1-8: Interruption for sync source change between a syncRef UE that is synchronized to GNSS directly or in-directly and another syncRef UE that is synchronized to GNSS directly or in-directly
  Follow Issue 3-1-x’s agreement
Issue 3-1-11: Interruption for sync source change between a syncRef UE that is synchronized to gNB/eNB directly or in-directly and another SyncRef UE that is synchronized to gNB/eNB directly or in-directly
  Follow Issue 3-1-x’s agreement
Issue 3-1-13: Interruption for sync source change between a syncRef UE that has the lowest priority and another SyncRef UE that has the lowest priority
  Follow Issue 3-1-x’s agreement
WF

## Slide 6
Issue 3-1-14 : Interruption due to source change between gNB and eNB
  Option 1: follow Issue 3-1-x’s agreement
  Option 2: not define
Issue 3-2 : Interruption for switching between LTE SL and NR SL
  RRM session can discuss the interruption requirement based on the switching time requirement agreed in RF session
  Rapporteur decides which session (RF or RRM) to discuss the starting point of switching for next meeting to avoid duplicated discussion
WF

## Slide 7
Terminology ‘S-RSRP’ vs ‘PSBCH-RSRP’
  Use PSBCH-RSRP based on current RAN1 spec.(38.215)
  Revisit if RAN1 has agreement to define S-RSRP other than PSBCH-RSRP
Band grouping
  Specify based on REFSENS in RF session.
  Add square bracket in RRM specification before the RF session’s conclusion
Side condition of received signal level
  dBm numbers and band groups in square bracket are pending REFSENS discussion in RF session. Come back to revise the numbers after RF session reaches agreement
  Changes are needed for B.6.4(TS36.133) to maintain consistent NR and LTE side conditions
WF

## Slide 8
NR V2X RRM part 2

## Slide 9
L1 SL-RSRP measurement
Agreement:
Refer on the RAN1/2 section to avoid detail procedure description for L1 SL-RSRP measurement in RAN4.
Define side condition for both PSCCH-RSRP and PSSCH-RSRP measurement accuracy with SNR ≥ 0dB.
Define the same requirements for both PSSCH-RSRP and PSCCH-RSRP.
If power boosting on DMRS multiple port is not applied, the PSSCH-RSRP shall be calculated by the sum of all transmission antenna ports.
Postpone discussion on the test case to the Perf part.
Open issues
Whether to have a general description of re-evaluation to introduce the usage of L1 SL-RSRP as legacy LTE V2X?
  Option 1: Yes
  Option 2: No
Absolute accuracy of L1 SL-RSRP measurement
    Option 1: ±4.5dB at SNR=0dB
    Option 2: ±5dB at SNR=0dB
Measurement requirements(1)

## Slide 10
S-RSSI measurement
  Reuse S-RSSI measurement accuracy in LTE-V2X.
S-SSB RSRP side condition
  Determine NR V2X measurement side conditions on S-SSB RSRP based on both NR V2X S-RSRP Es/Iot and the agreed receiver sensitivity requirement per band group in RF session.
Measurement requirements(2)

## Slide 11
Core requirements (based on work-split in last year)
Measurement accuracy requirements
Annex B.4
CR work-split for RAN4#95-e meeting
Section | Company
12.1 ~ 12.8 : Editorial Change | LG Electronics
12.5 L1 SL-RSRP measurements | Qualcomm
12.7 Interruption | CATT
3.5.2 NR operating bands in FR1 | LG Electronics
Section | Company
10.4 V2X Measurements 10.4.1 Introduction 10.4.2 Intra-Frequency PSBCH-RSRP Measurement Accuracy Requirements for FR1 | Huawei
10.4.3 Intra-Frequency SL-RSSI Measurement Accuracy Requirements for FR1 10.4.4 Intra-Frequency L1 SL-RSRP Measurement Accuracy Requirements for FR1 | LG Electronics
Section | Company
B.4 Conditions for V2X B.4.1 Test parameters for GNSS signals B.4.2 Conditions for PSBCH-RSRP Accuracy Requirements B.4.3 Conditions for Selection/Reselection to Intra-frequency SyncRef UE B.4.4 [Conditions for PSCCH-RSRP Accuracy Requirements] | LG Electronics