## Slide 1: Way forward on multiple SCell activation
Apple, …
R4-2005347
3GPP TSG-RAN WG4 Meeting #94-e-bis
Electronic Meeting, 20 – 30 Apr., 2020
Agenda item: 6.15
Document for: Approval

## Slide 2: Requirement scope of multiple SCell activation (sub-topic 1-1 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  Do not consider interruption between LTE SCell activation and NR SCell activation in EN-DC and NE-DC cases for RRM requirement
  Do not define requirement of multiple SCell activations in different CGs for UE without per-FR MG capability in NR-DC
  To define requirement of multiple SCell activations of if to-be-activated SCells includes FR1 unknown and FR1 known SCells (with ≤160ms Scell_meas_cycle and/or with >160ms Scell_meas_cycle) on the same band
      AGC settling time is: TFirstSSB_MAX, if on that band UE has at least one FR1 known Scell with the SCell measurement cycle larger than 160ms to be activated but does not have any FR1 unknown Scell to be activated
      AGC settling time is: TFirstSSB_MAX + TSMTC_MAX , if on that band UE has at least one FR1 unknown Scell to be activated

## Slide 3: MAC PDU processing delay (sub-topic 1-2 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  In NR-DC scenario, if two MAC PDUs on dual NR CGs are received for multiple SCell activation, the MAC processing and application time shall be 3ms.

## Slide 4: delay extension due to interruption on L1-RSRP measurement resource (sub-topic 1-3 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  When one single MAC CE is received for multiple SCell activation in EN-DC, NE-DC, NR SA and one CG of NR-DC, there is no interruption on the L1-RSRP measurement resource of the target to-be-activated SCell and no additional delay extension is needed
  When multiple SCells activation happens in two CGs of NR-DC
    RAN4 only defines multiple SCell activation requirement for per-FR-MG-capable UE, and there is no interruption on the L1-RSRP measurement resource of the target to-be-activated SCell in FR2 and no additional delay extension is needed
    RAN4 to not define multiple SCell activation requirement for per-UE MG capable UE where L1-RSRP measurement in FR2 is interrupted due to another SCell activation in FR1

## Slide 5: Scaling factor for cell detection time of target being-activated SCell (sub-topic 1-4 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  FFS:
    FR1 unknown SCell that is contiguous to FR1 known cell or FR1 active serving cell is not accounted for, or scaled by, N when either of the following is fulfilled:
      A single SSB is used in the SCell,
      Multiple SSBs are used in the SCell, and TCI state indication for PDCCH is received with the SCell activation MAC PDU
    Otherwise the SCell is accounted for in, and scaled by, N.
  FFS:
    Option 2 (MediaTek, Ericsson, Qualcomm): “cell detection time” in delay extension due to searcher limitation means “1*TRS” for FR1 unknown SCell and “8*Trs” for the FR2 unknown Scell
    Option 3 (NEC, Huawei, Apple): “cell detection time” in delay extension due to searcher limitation means “TFirstSSB_MAX + TSMTC_MAX + Trs” for FR1 unknown SCell and “TFirstSSB + 23*Trs” for the FR2 unknown Scell

## Slide 6: Interruption(s) on other serving cells when multiple SCells are being activated (sub-topic 1-5 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  if there is one single MAC CE for multiple SCell activation received in one CG, the UE RF tuning(s) for SCell activation in this CG shall not extend any SCell activation delay in this CG.
  Do not need to define new interruption length requirement for multiple SCell activation scenario. Interruption length can re-use those for single SCell activation

## Slide 7: Interruption to AGC settling (sub-topic 1-6 in R4-2005293) (1/2)
Agreement in RAN4 #94-e-bis:
  When one single MAC CE is received for multiple SCell activation in EN-DC, NE-DC, NR SA and one CG of NR-DC
    No RF tuning interruption is expected to occur during AGC settling time in R16 multiple SCell activation delay requirement.
    There is no additional interruption and delay extension due to AGC interruption when the aggressor SCells being activated are inter-band FR1 SCells
  When two MAC PDUs are received on two CGs for multiple SCells activation in NR-DC
    Since RAN4 only defines multiple SCell activation requirement for per-FR MG capable UE when two MAC PDUs are received on two CGs in NR-DC, no RF tuning interruption is expected to occur during AGC settling time in R16 multiple SCell activation delay requirement.

## Slide 8: Interruption to AGC settling (sub-topic 1-6 in R4-2005293) (2/2)
Agreement in RAN4 #94-e-bis:
  RAN4 shall apply the same R15 criteria to multiple SCell activation as single SCell for AGC extension in FR1 and FR2.
    If multiple SCell activation in FR1 intra-band,
      If at least one of the aggressor SCells being activated is unknown cell, the victim SCell activation delay may be extended to TFirstSSB_MAX+ TSMTC_MAX.
      If all SCells are known cell and the measurement cycle>160ms for at least one of the aggressor SCells being activated, the victim SCell activation delay may be extended to TFirstSSB_MAX.
    If multiple SCell activation in FR2 intra-band and there is no active serving cell on the FR2 band and,
      If at least one of the aggressor SCells being activated is known cell and the victim SCell is unknown cell, the victim SCell activation delay may be changed from 24*Trs to 0.
      If at least one of the aggressor SCells being activated is unknown cell and the victim SCell is known cell, the victim SCell activation delay may be unchanged.

## Slide 9: mixed unknown and known to-be-activated Scells in FR2 (sub-topic 1-7 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  If there is no active serving cell on the FR2 band and if the target SCells being activated are unknown to UE,
    Only one unknown SCell shall execute L1-RSRP measurement and reporting;
    Other unknown SCells shall hold on its activation procedure until their TCI states are configured;
    Only single interruption due to single RF tuning is considered.
  If there is no active serving cell on the FR2 band and if at least one of the target SCells being activated is known cell and at least one of the target SCells is unknown cell,
    All unknown SCell won’t need L1-RSRP measurement and reporting;
    All unknown SCells shall hold on its activation procedure until their TCI states are configured;
    Only single interruption due to single RF tuning is considered.

## Slide 10: Delay extension of multiple SCells activation for inter-band FR2 CA (sub-topic 1-8 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  Defer the multiple SCell activation requirement design for inter-band FR2 CA until RAN4 completes the requirement of single Scell activation in inter-band FR2 CA.

## Slide 11: Multiple SCell de-activation delay (sub-topic 1-9 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  The SCell deactivation delay requirements with multiple downlink SCells remain the same with the single SCell deactivation relay requirements

## Slide 12: Multiple SCell activation delay when only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC (sub-topic 1-10 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  FFS: activation delay for FR1 known SCell with Scell_meas_cycle≤160ms (options in issue 1-10-1 in R4-2005293)
  FFS: activation delay for FR1 known SCell with Scell_meas_cycle>160ms (options in issue 1-10-2 in R4-2005293)
  FFS: activation delay for FR1 Unknown SCell (options in issue 1-10-3 in R4-2005293)
  Agreement: activation delay for “FR2 SCell with active serving cell(s) on same band and with configured SMTC” is same as single SCell activation (in issue 1-10-4 in R4-2005293)
  Agreement: activation delay for “FR2 SCell with active serving cell(s) on same band but without configured SMTC” is same as single SCell activation (in issue 1-10-5 in R4-2005293)
  Agreement: activation delay for “FR2 known SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting, and UE receives the SCell activation command, semi-persistent CSI-RS activation command and TCI state activation command at the same time” is same as single SCell activation (in issue 1-10-6 in R4-2005293)
  Agreement: activation delay for “activation delay for FR2 known SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting, and UE receives TCI state activation command after SCell activation command” is same as single SCell activation (in issue 1-10-7 in R4-2005293)
  Agreement: activation delay for “activation delay for FR2 known SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting” is same as single SCell activation (in issue 1-10-8 in R4-2005293)
  FFS: activation delay for FR2 unknown SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting (options in issue 1-10-9 in R4-2005293)
  FFS: FR2 unknown SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting (options in issue 1-10-10 in R4-2005293)

## Slide 13: Multiple SCell activation delay when two MAC PDUs on dual NR CGs are received within 3ms for multiple SCell activation in two CGs of NR-DC for per-FR MG capable UE (sub-topic 1-11 R4-2005293)
Agreement in RAN4 #94-e-bis:
  reuse same requirement as in sub-topic 1-10 scenario (from issue 1-10-1 to issue 1-10-5), and no unknown FR2 Scell shall be considered.

## Slide 14: Others (sub-topic 1-12 and 1-13 in R4-2005293)
Agreement in RAN4 #94-e-bis:
  Multiple SCell activation delay when in NR-DC the time gap between two MAC PDUs received on dual NR CGs is greater than 3ms for multiple SCell activation, but the second MAC PDU for SCell activation in one CG was received within the activation period of the SCell(s) activation in other CG (options in issue 1-12 in R4-2005293):
    reuse same requirement as in sub-topic 1-11 scenario.
  Multiple SCell activation delay when two MAC PDUs are received for multiple SCell activation in two CGs of NR-DC for per-UE MG capable only UE (options in issue 1-13 in R4-2005293)
    No need to consider this requirement

## Slide 15: FFS: narrow down multiple Scell activation cases for requirements
  Continue the discussion on how to down select the cases for multiple SCell activation requirement in next RAN4 meeting; and if conclusion is made in next meeting to preclude certain case(s), the corresponding requirement for that case(s) could be removed.

## Slide 16: Draft CR plan for next RAN4 meeting
Companies are encouraged to bring in drafts CRs in next RAN4 meeting on following aspects:
  Multiple NR SCell activation/deactivation delay requirement to TS38.133
  Multiple NR SCell activation/deactivation interruption requirement to TS38.133, if needed
  Multiple NR SCell activation/deactivation interruption requirement to TS36.133, if needed
  Others, if needed