## Slide 1: WF on inter-frequency without MG
CMCC
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Online, 20 – 30 Apr., 2020
R4-2005348

## Slide 2: Background
R4-2002250 WF on inter-frequency without MG was agreed in RAN4#94e meeting
R4-1915853 WF on inter-frequency without MG was agreed in RAN4#93meeting.

## Slide 3: Issue 2-1: Capability of supporting inter-frequency measurement without MG
  Option 1 (vivo, MediaTek, OPPO, Huawei, Qualcomm, vivo, Intel, Ericsson) : Optional with UE capability signaling
  Option 2 (CMCC): Mandatory with UE capability signaling

## Slide 4: Issue 2-2: Assumption of searcher numbers
For UE without CA capability, the number of search assumed in the requirement is 1

## Slide 5: Issue 2-3: How to handle the backward compatible issue for network
  Explicitly enable “inter-frequency measurement without MG” feature with a release 16 configuration flag
    If network configures the flag, when SMTC is partially overlapped with network configured MG, UE perform inter-frequency without MG measurement outside gap
    If network does not configure the flag, when SMTC is partially overlapped with network configured MG, UE perform inter-frequency measurement within gap.

## Slide 6: Issue 2-4: UE behaviour for inter-frequency measurement w/o MG partially overlapped with MG
For CA capable UE :
  Define requirements based on the assumption that UE perform measurement outside gaps (same as intra-frequency measurement without MG)
For non-CA capable UE:
  Option 1 (Apple, CMCC, vivo, OPPO, Intel, Huawei, Ericsson, Qualcomm): Define requirements based on the assumption that UE perform measurement within gaps
  Option 2 (MTK): Define requirements based on the assumption that UE perform measurement outside gaps (same as intra-frequency measurement without MG)

## Slide 7: Issue 2-5: Scheduling restriction for inter-frequency measurement w/o MG
Clarify in the spec that synchronization is assumed for overlapped TDD carriers. (last meeting agreement)
When UE performs inter-frequency measurements without measurement gaps in a TDD bands on FR1 and FR2:
  UE can assume following 2 conditions are fulfilled:
    SFN and frame boundary across serving cell and inter-frequency neighbor cells is aligned, and
    the timing of SSBs across serving cell and inter-frequency neighbor cells are aligned
  UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols to be measured, and on 1 data symbol before each consecutive SSB symbols to be measured and 1 data symbol after each consecutive SSB symbols to be measured within SMTC window duration

## Slide 8: Issue 2-6: Scheduling restriction when the target SSB has a different SCS grid
Option 1 (MediaTek, OPPO, Qualcomm):
  When the target SSB has a different SCS grid as that of UE’s serving cell, UE is allowed to have scheduling restriction in the entire SMTC duration.
Option 2 (Huawei, Apple, CMCC, Huawei, Ericsson):
  No need to specify the scheduling restriction for the case the target SSB has a different SCS grid as that of UE’s serving cell.

## Slide 9: Issue 2-8: Update the UE capability simultaneousRxDataSSB-DiffNumerology
Option 1 (CMCC, Apple, MediaTek, vivo, OPPO, Intel, Huawei, Ericsson):
  To update the UE capability simultaneousRxDataSSB-DiffNumerology to indicate whether the UE supports concurrent intra-frequency measurement on serving cell or neighbouring cell or inter-frequency measurement without measurement gap and PDCCH or PDSCH reception from the serving cell with a different numerology as defined in clause 8 and 9 of TS 38.133
Option 2 (Qualcomm):
  Introduce a new UE capability to indicate whether the UE supports concurrent inter-frequency measurement without measurement gap and PDCCH or PDSCH reception from the serving cell with a different numerology as defined in clause 8 and 9 of TS 38.133
Agreement: Keep both options in the LS, and let RAN2 make the decision