## Slide 1: WF on NR-U RRM Requirements (Part 2) (All agreements in RAN4#94-e-Bis in email thread #105)
MediaTek inc.
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005367
Electronic Meeting, April 20-May 1, 2020
Agenda Items: 6.1.5.2, 6.1.5.8, 6.1.5.9, 6.1.5.10, 6.1.5.13

## Slide 2
Agreements from the 1st round
Agreement from GTW session
Agreements from the 2nd round

## Slide 3: Topic #1: Cell re-selection (AI 6.1.5.2)
Do not specify the maximum number of times when any of Md,max, Mm,max, and Me,max is exceeded before the UE initiates cell selection procedures for the selected PLMN
Paging interruption time shall not exceed TSI,CCA + 2*[Ttarget_cell_SMTC_period] ms. TSI,CCA is the time required to acquire the SI when the operating carrier is subject to CCA failures. FFS how to address unavailable SMTC occasion at UE in Ttarget_cell_SMTC_period
  FFS if there is any impact on Ttarget_cell_SMTC_period
FFS: clarification of unavailable SMTC
Postpone the side condition discussion to performance part
For a cell that is already identified, after N unsuccessful measurement attempts due to exceeding the max number of unavailable SMTC occasions, UE needs to detect the cell again. FFS the value N and the target cell/carrier to initiate the cell detection procedure
Replace Kcarrier * Tdetect,NR_Inter by Kcarrier * Tdetect,NR_Inter + Kcarrier_CCA * Tdetect,NR_Inter_CCA

## Slide 4: Topic #3: Active BWP switching (AI 6.1.5.9)
The UL BWP switching delay upon detection of consistent UL LBT failure is the same as the delay of DCI and timer based BWP switching
The interruption requirement (starting time and duration) of UL BWP switching upon detection of consistent UL LBT failure follow existing interruption requirements for DCI and timer based BWP switch
Upon detecting consistent UL LBT failure at slot#n when UE detects lbt-FailureInstanceMaxCount number of LBT failure within lbt-FailureDetectionTimer, UE starts UL BWP switch at slot#n+1
The ending point of UL BWP switching delay upon detection of consistent UL LBT failure
  Option 1: UE transmits RACH
  Option 2: UE is ready to transmit RACH
FFS whether to add the condition about the relative frequency locations for the old and new UL BWPs

## Slide 5: Topic #4: RLM and link recovery procedures (AI 6.1.5.10)
The set of SSBs that UE is required to monitor
  Define the following UE capabilities
    For RLM/BFD/CBD UE is required to monitor at least N1 candidate SSB positions from the set of SSBs that are QCLed with each other within the set of configured resources
    For intra and inter-frequency measurements UE is required to monitor at least N2 candidate SSB positions from the set of SSBs that are QCLed with each other within SMTC
      FFS for the case Q is not provided to the UE
      FFS how to handle IDLE mode capabilities
    Candidate N1 and N2 values are [1, 2, …]
    FFS whether N1 = N2
    FFS whether to have different capabilities for FBE and LBE modes
  Send LS to RAN1 to ask for feedback on candidate values N1 and N2 taking into account impact on the overall system performance
  Further discuss other cases
For both LBE and FBE, RLM requirements shall not rely on COT

## Slide 6: Topic #4: RLM and link recovery procedures (AI 6.1.5.10)
OOS evaluation period for SSB-based RLM
  Option 2: OOS evaluation is based on Lout, where Lout ≤Lout,max is the number of SSBs not available at the UE during TEvaluate_out_SSB
  Option 3: The evaluation period is scaled by a fixed scaler
    FFS: excluding samples whose SNR is higher than X dB
Whether UE can expect gNB to transmit RLM-RS with same transmit power across different occasions
  Send LS to RAN1 in RAN4#95-e meeting about the observation from RAN4 perspective about concern on transmit power of RS
In RAN4#95-e meeting, RAN4 decides whether to keep working on CSI-RS based RLM requirement in Rel-16
CBD requirement: Take the proposal for SSB-based CBD in R4-2004032 as the starting point. FFS the exact numbers

## Slide 7: Topic #5: Timing (AI 6.1.5.13)
If the UE uses a reference cell on a carrier frequency subject to CCA for deriving the UE transmit timing, then the UE shall meet all the transmit timing requirements provided that
  Option 1: at least N SSB are available at the UE during the last 160 ms
    N=TBD
    Definition of available cell/SSB is pending on RAN1 feedback to LS R4-2005418 on the number of candidate SSB positions from the set of SSBs to be monitored