## Slide 1: WF on RRM requirements for Tx switching between two uplink carriers
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, 20 – 30 Apr., 2020
      R4-2005416
Document for: Approval

## Slide 2: Background
Session chair: Further discuss the DL interruption parameters under assumption that DL interruptions are allowed. If the RF session reaches the conclusion that interruptions are not allowed, then the requirements will not be added to specs.

## Slide 3: WF on RRM requirements for Tx switching between two uplink carriers
whether need to capture the applicability for DL interruption requirements in 38.133/36.133.
Agreement: If the DL interruptions are allowed and the DL interruption applicability is agreed to be captured in RF specification, RRM can directly refer to RF spec. Otherwise, the DL interruption applicability is captured in RRM spec.
The DL interruption granularity is in the unit of OFDM symbols.

## Slide 4: DL interruption length
DL interruption length
- Option 1
  For FDD-TDD uplink CA, UE is allowed to cause X OFDM symbols DL interruption on NR carrier(s), depending on UE capability
u | NR slot length (ms) of victim cell | UL switching period |  | 
 |  | 35us | 140us | 210us
0 | 1 | 2 | 3 | 4
1 | 0.5 | 2 | 5 | 7
2 | 0.25 | 3 | 9 | 13
  For inter-band EN-DC, UE is allowed to cause DL interruption of Y OFDM symbols on LTE carriers, depending on UE capability
UL switching period | 
35us | 140us
2 | 3
  For inter-band EN-DC, UE is allowed to cause DL interruption of Z OFDM symbols on NR carriers, depending on UE capability
u | NR slot length (ms) of victim cell | UL switching period | 
 |  | 35us | 140us
0 | 1 | 2 | 3
1 | 0.5 | 2 | 5
2 | 0.25 | 3 | 9
  Note: DL interruption time in the unit of us is not larger than UL switching time agreed in RF session.

## Slide 5: DL interruption length
- Option 2
  DL Interruption length is
u | NR slot length (ms) of victim cell | UL switching period |  | 
 |  | 35us | 140us | 210us
 |  | Uncertainty UL switching window |  | 
 |  | 101us | 206us | 276us
0 | 1 | 3 | 5 | 5
1 | 0.5 | 4 | 7 | 9
2 | 0.25 | 7 | 13 | 17

## Slide 6: WF on RRM requirements for Tx switching between two uplink carriers
The DL interruption location/Starting point
  Option 1: the DL interruption are the OFDM symbols fully or partial overlapped with the UL switching period.
  Option 2: the starting time is determined by TA+TA uncertainty+MRTD