## Slide 1: Way forward on Rel-15 NR UE Performance Maintenance
Qualcomm, …
3GPP TSG-RAN WG4 Meeting #94-e-Bis
E-meeting, 20 April – 30 April, 2020
Agenda Item: 4.11.1
R4-2005517

## Slide 2: PDCCH Mapping to Physical Antennas and Precoder Configuration
For CSI reporting requirements, PDCCH is precoded with random single panel Type I precoder to two physical antennas when number of Tx antennas are > 1.
  In case of static channel, precoder will be randomly chosen from precoder index 0 and 2.
  Precoder will be randomly chosen per slot.
For Sustained Data Rate requirements with 2Tx, PDCCH precoder will be randomly chosen per slot from precoder index 0 and 2.

## Slide 3: DL Channels Mapping
Specify antenna port to physical antenna mapping in Annex B.4.1.
Clarification on definition of EPRE will be provided in Table C.3.1-1 and Table C.5.1-1:
  Companies are encouraged to check EPRE definition in TS 38.214 (i.e. per port or for all ports, before or after precoder etc.)
EPRE ratios in Annex C are determined such that powerControlOffset and powerControlOffsetSS are set to 0.

## Slide 4: MIMO Correlation Matrices
MIMO correlation matrices for cross polarized 2x4 and 4x4 high correlation cases will be specified in Table B.2.3.2.2-2.