## Slide 1: WF on PDSCH demodulation requirement and General aspects for NR eMIMO
Samsung
3GPP TSG-RAN4 Meeting #94e-b
Electronic Meeting, April.20th - .April 30th 2020
Agenda item: 6.11.3
R4-2005529
Document for: Approval

## Slide 2: Background
Agreed WFs for demodulation requirement for NR eMIMO WI in previous meetings
  R4-2002419 WF on demodulation and CSI requirement for NR eMIMO, RAN4#94-e
  R4-2002420 WF on PDSCH demodulation requirements based on multi-TRP transmission for NR eMIMO, RAN4#94-e

## Slide 3: Test Scope of Enhancement on low PAPR RS requirement
No new PDSCH requirement with Rel-16 DMRS enhancement for CP-OFDM
No new PUSCH requirement with Rel-16 DMRS enhancement for CP-OFDM

## Slide 4: Test Scope of PDSCH requirement with multi-TRP/Panel for eMBB
FFS to define PDSCH requirement scheduled by single-DCI based multi-TRP/Panel transmission for eMBB
Applicability rule
  FFS on test applicability rule between single-DCI and multi-DCI based multi-TRP/Panel transmission for conducting the tests based on UE capability

## Slide 5: General test setup for PDSCH requirements with multi-TRP/Panel for eMBB
Test scenario
  FR1: Define PDSCH requirement with cover scenarios with simultaneous reception from multi-TRP/Panel for eMBB
  FR2:
    No PDSCH requirements with serval impendent Rx beam and simultaneous reception from multi-TRP/Panel for eMBB in FR2
    FFS on define PDSCH with covering scenarios with only 1 Rx beam with and simultaneous reception from multi-TRP/Panel for eMBB
SCS and CBW
  FR1
    FDD SCS =15KHz, 10 MHz
    TDD SCS =30KHz, 40 MHZ
  FFS for FR2
    TDD SCS =120KHz, 100 MHz

## Slide 6: General test setup for PDSCH requirements with multi-TRP/Panel for eMBB
TCI state configuration and QCI-info for FR1
TCI index | Information |  | FR1
TCI state #0 | Type 1 QCL information | SSB index | SSB #0
 |  | QCL Type | Type C
 | Type 2 QCL information | SSB index | N/A
 |  | QCL Type | N/A
TCI state #1 | Type 1 QCL information | CSI-RS resource | CSI-RS resource 1 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type A
 | Type 2 QCL information | CSI-RS resource | N/A
 |  | QCL Type | N/A
TCI state #2 | Type 1 QCL information | CSI-RS resource | CSI-RS resource 2 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type A
 | Type 2 QCL information | CSI-RS resource | N/A
 |  | QCL Type | N/A

## Slide 7: General test setup for PDSCH requirements with multi-TRP/Panel for eMBB
FFS on TCI state configuration and QCI-info for FR2
TCI index | Information |  | FR2
TCI state #0 | Type 1 QCL information | SSB index | SSB #0
 |  | QCL Type | Type C
 | Type 2 QCL information | SSB index | SSB #0
 |  | QCL Type | Type D
TCI state #1 | Type 1 QCL information | CSI-RS resource | CSI-RS resource 1 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type A
 | Type 2 QCL information | CSI-RS resource | CSI-RS resource 1 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type D
TCI state #2 | Type 1 QCL information | CSI-RS resource | CSI-RS resource 2 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type A
 | Type 2 QCL information | CSI-RS resource | CSI-RS resource 1 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type D

## Slide 8: General test setup for PDSCH requirements with multi-TRP/Panel for eMBB
Assumption for UE receiver implementation
  The test case design should be ensure receiver implementation agnostic with assumption of single FFT operation
Set BS antenna correlation between two TRPs as 0
Separate decoding of each PDSCH scheduled by multi-DCI
FFS on consider the scenario with TRS/CSI-RS collide between

## Slide 9: General test setup for PDSCH requirements with multi-TRP/Panel for eMBB
Timing offset configuration
  Define with timing offset between two TRPs, the timing offset setting should be ensured that all paths from TRPs are within CP
  FFS on Set timing offset by scaled with SCS

## Slide 10: General test setup for PDSCH requirements with multi-TRP/Panel for eMBB
Timing offset configuration
  Study suitable upper bounds on propagation delay difference. The following values can be used from LTE Rel-11 CoMP (-0.5us and 2us) as a starting point
    FR1 FDD (15KHz SCS)
      Positive upper bound
        Option 1: [2] us
        Other options are not precluded
      FFS on Negative upper bound
    FR1 TDD (30KHz SCS)
      Positive upper bound
        Option 1: [1] us
        Option 2: [2] us
        Other options are not precluded
      FFS on Negative upper bound
    FFS on FR2 TDD (120 KHz)
      Positive upper bound
        Option 1: [0.25] us
        Other options are not precluded
      FFS on Negative upper bound

## Slide 11: General test setup for PDSCH requirements with multi-TRP/Panel for eMBB
Frequency offset configuration
  FFS on set frequency offset by scaled with SCS
  Study suitable frequency offset configuration with considering [0.1]ppm frequency error. The following values can be used a starting point
    FR1
      FDD (15KHz SCS) :
        Option 1: 200 Hz
        Option 2: 300Hz
        Other options are not precluded
      TDD (30KHz SCS):
        Option 1 :300 Hz
        Option 2: 600 Hz
        Other options are not precluded
    FFS on FR2
      TDD (120KHz SCS): (0~600 Hz)
      Other options are not precluded

## Slide 12: General test setup for PDSCH requirements with multi-TRP/Panel for eMBB
TDD pattern
  FR1
    TDD (30KHz SCS): 7DS2U
  FFS for FR2
Number of HARQ process
  FR1
    FDD (15KHz SCS): 4
    TDD (30KHz SCS)
      Option 1: The total number of HARQ process should be limited and not larger then 16
        TDD (30KHz SCS) 7DS2U : 8; 8+8=16
      Other options are not precluded
  FFS for FR2

## Slide 13: General test setup for PDSCH requirements multi-DCI with multi-TRP/Panel for eMBB
HARQ-ACK
  Both separate and joint HARQ-ACK feedback can be used in the test setup based on UE capability
  PDCCH scheduling
  Configure 2 CORSET pool index for multi-DCI on multi-TRP
    Two CORSET pool index with 0 and 1, each TRP PDCCH with symbol #0 and symbol #1 in time domain and FDMed half bandwidth
  Configure different scrambling sequences for PDSCH scheduled by Multi-DCI

## Slide 14: General test setup for PDSCH requirements multi-DCI with multi-TRP/Panel for eMBB
UE rate-matching behavior
  FFS on define PDSCH requirement for UE rate-matching around a configured CRS pattern

## Slide 15: General test setup for PDSCH requirements multi-DCI with multi-TRP/Panel for eMBB
Whether to define PDSCH requirements for other scheduling schemes
  Option 1: at least partial overlapping
      Option 1a: Both partial overlapping and full-overlapping
  Option 2: only non-overlapping
  Option 3: Non-overlapping and full-overlapping if no requirements for single-DCI based multi-TRP will be introduced, Otherwise only non-overlapping
  Option 4: Non-overlapping and partial overlapping if overlapping requirements for single-DCI based on multi-TRP will be introduced, Otherwise both partial and full-overlapping

## Slide 16: Test parameters for layer combination for non-overlapping scheduling
Layer combination configuration
  2 Rx UE
    2+2
  4 RX UE
    2+2

## Slide 17: Test configuration for PDSCH with non-overlapping
PDCCH configuration
  Option 1:
    CORESETPoolIndex =0, 1, each with one COREST configured for each PDCCH
      Symbols for PDCCH：0,1
      Number of PRB, Half of the channel bandwidth with contiguous RB allocation and non-interleaved CCE-to-REG mapping
      K0=0
      AL=8
  Other options not precluded

## Slide 18: Test configuration for PDSCH with non-overlapping (Continue)
PDSCH configuration
  Option 1
    PDSCH resource mapping type: Type A
    Resource allocation type: Type 1
    DM-RS: DM-RS configuration type 1 with single-symbol DM-RS: 1+1
    Antenna ports index: such as {1000,1001} and {1002,1003}, i.e. different CDM groups for two TRPs
    Starting symbol (S): 2
    Time duration (L): 12
    Frequency domain: half of the maximum bandwidth by indicating the start resource block , the allocated resource blocks
  Other options not preclude

## Slide 19: Test configuration for PDSCH with non-overlapping (Continue)
PDSCH configuration
  Option 1
    Layer combination: 2+2
    Number of HARQ process
      FR1 FDD (15KHz SCS): 4
      FR1 TDD (30KHz SCS): 7DS2U with 8, as per the current configuration, 8+8=16 HARQ process
    Timing offset and frequency offset
      2 us for 15KHz SCS, 1 us for 30KHz SCS
      200Hz for 15KHz SCS, 400Hz for 30KHz SCS
  Other options not preclude

## Slide 20: Test parameters for PDSCH requirement with Single-DCI based(if single-DCI introduced)
Resource allocation
  full-overlapping
  Layer combination
  2 Rx UE
    1+1
  4 RX UE
    1+1
  Number of TCI state
  Two TCI states configuration

## Slide 21: Test Scope of PDSCH requirement with single DCI based multi-TRP/Panel for URLLC
FFS on defined PDSCH requirement for single-DCI based URLLC (reliable) multi-TRP/Panel transmission schemes
FFS on test metric for requirement definition
  Option 1: 70% @max achievable throughput
  Option 2: 1% BLER
FFS on test scenario for URLLC
  Option 1:
    For FR1: consider simultaneous and non-simultaneous reception from multi-TRP/Panel
    For FR2: consider non-simultaneous reception from multi-TRP/Panel with single Rx beam at transmission occasion
  Other options are not precluded:

## Slide 22: URLLC transmission schemes and applicability rule(if URLLC requirement is agreed)
URLLC transmission schemes
  Option 1: 1a; FFS scheme 2a, 2b; Deprioritize scheme 3,4
  Option 2: 1a, 2a, 2b, 3, 4
  Option 3: 2a, 3, 4
  Other options are not precluded
Applicability rule
  FFS on applicability rule between URLLC transmission schemes
  FFS on applicability rule between eMBB and URLLC transmission schemes