## Slide 1
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005532
Electronic Meeting, 20 – 30 Apr., 2020
Agenda Item: 6.17.2.1
WF on UE demodulation for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1910050 WF on demodulation for UE NR HST, RAN4#92
  R4-1912808 Way forward on NR HST UE demodulation, RAN4#92BIS
  R4-1915926 WF on UE demodulation for NR HST, RAN4#93
  R4-2002418 WF on UE demodulation for NR HST, RAN4#94-e

## Slide 3: HST-SFN
Maximum Doppler frequency
  For TDD 30 KHz SCS, 500km/h
    1667Hz
      larger implementation margin of 1 dB instead of 0.5dB being added on top of average impairment simulation results
  For FDD 15 KHz SCS, 500km/h
    Option 1 (Qualcomm): 851Hz
    Option 2 (CMCC, Intel, Huawei, DoCoMo) : 870Hz
Whether to schedule in TDD special slot for HST-SFN
  Do not schedule data in TDD special slots in HST-SFN test cases to achieve maximum throughput

## Slide 4: HST-SFN
Whether to introduce requirements for target speed of 350km/h for HST-SFN
    Do not define requirements for target speed of 350km/h for HST-SFN
Antenna configuration for HST-SFN
    Define requirements for both 2x2 and 2x4, and reuse the existing test applicability rule of NR release 15 UE normal PDSCH performance requirements

## Slide 5: HST single tap
Maximum Doppler frequency
  For 15KHz SCS, 500km/h
    Option 1 (CMCC, Qualcomm, Ericsson, DOCOMO): 1250Hz
    Option 2 (Samsung, Intel, Huawei, vivo): 870Hz
    Option 3 (CMCC, HW, Ericsson, DOCOMO): 972Hz
Antenna configuration for HST single tap
    Define requirements for both 1x2 and 1x4, and reuse the existing test applicability rule of NR release 15 UE normal PDSCH performance requirements

## Slide 6: HST single tap
HST single tap requirements definition
  Do not mandate the specific TRS processing for requirement definition and left it up to company decision
    Option 1 (CMCC, Huawei, Samsung, vivo, Ericsson, DOCOMO, Qualcomm): Do not provide signalling during the HST single tap demodulation test
    Option 2(Intel): Provide HST RRM signalling during the demodulation test to inform UE about HST conditions to enable switch to single shot processing.

## Slide 7: Multi-path fading channel
MCS for multi-path fading channel
  MCS13
Antenna configuration for multi-path fading channel
    Define requirements for both 2x2 and 2x4, and reuse the existing test applicability rule of NR release 15 UE normal PDSCH performance requirements

## Slide 8: Multi-path fading channel
Scheduling in TDD special slot for multi-path fading
  do not schedule data in TDD special slots.

## Slide 9: Transmission scheme
DPS transmission scheme 1 (including 1a and 1b)
  Further discuss the test case design for DPS transmission scheme 1, and verify whether new specific UE receiver processing from demod aspect required compared to UE to handle HST-single Tap and HST-SFN channel model.
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 10: Transmission scheme
Transmission scheme 2
  Discuss transmission scheme 2 in eMIMO WI first, then discuss transmission scheme 2 in HST-SFN deployment scenario later after the parameters in eMIMO WI are finalized and HST WI has sufficient TUs for discussion.
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 11: Transmission scheme
Transmission scheme 3
  No more discussion and treatment for transmission scheme 3 in Rel-16 HST WI.
  Regarding benefits observation: “capture in session note for information”:
    During RAN4 discussion for transmission schemes 3, RAN4 no conclusion for the benefit due to lack of enough input from companies also lack of involvement of RAN1/RAN2; there is one observation from single company Link-level evaluation results show that transmission schemes 3 provide potential performance benefits for HST scenario.
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 12: Release independent
Whether Rel.16 HST requirements can be release independent from Rel-15
    HST Multi-path fading tests can be release independent from Rel-15
    HST single tap tests can be release independent from Rel-15 if HST RRM signaling is not provided in the demodulation test
    Further study whether HST-SFN tests can be release independent from Rel-15
      send LS to RAN2 to check ‘early implementation approach is also applicable for NR

## Slide 13: Applicability rule
FFS the applicability rule between HST-SFN, HST single tap and HST multi-path fading performance test cases
FFS whether to define to Applicability rule between different Doppler frequencies for the same channel model

## Slide 14: HARQ process number
Adopt HARQ process number 4 for FDD and HARQ process number 8 for TDD with pattern 7D1S2U, as defined for HST in NR Rel-15

## Slide 15: UE capabilities/features
For HST-SFN
  Introduce per-UE capability to support enhanced demodulation performance for HST-SFN joint transmission scheme with velocity up to 500km/h. (Agreement in RAN4#93)
  For HST fading channel requirements, take it as mandatory requirements for Rel-16 and no capability signaling will be introduced.
  For HST single Tap channel demodulation requirements, no capability signaling will be introduced
  FFS whether requirements will be mandatory or optional
Further discuss whether feature list will be introduced for HST fading channel, and HST single Tap

## Slide 16: Updated simulation assumption for HST-SFN
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 13 based on 64QAM table | 
Propagation condition | HST-SFN | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 870Hz Option 2: 851Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 17: Updated simulation assumption for HST-single tap
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 1×2; 1×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
MCS | MCS 17 based on 64QAM table | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
Propagation condition | HST-single tap | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds= 300m, Dmin=2m | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 1250Hz Option 2: 870Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 18: Simulation assumption for multi-path fading channel
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 4; MCS 13; MCS 17 based on 64QAM table | 
Propagation condition | TDL-C 300ns | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 600Hz | 1200Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 19: Annex
Candidate transmission scheme to be further studied
  Transmission scheme 1 - DPS: PDSCH is only transmitted from one TRP at one time
    Transmission scheme 1a: UE only needs to track 1 TCI state (detail can be found in R4-1911003)
    Transmission scheme 1b: UE needs to track more than 1 TCI states (detail can be found in R4-1911091)
  Transmission scheme 2 - PDSCH is jointly transmitted from two or more adjacent TRPs scheduled by multi-DCI(detail can be found in R4-1911091)
  Transmission scheme 3 - Joint transmission + Distributed reference signal (detail can be found in R4-1911003)
    joint transmission + Distributed TRS
    joint transmission + Distributed DMRS